600 Suffolk Street	Tel  (978) 934-4903

Lowell, MA 01854	Fax (978) 459-7915

http://ulcar.uml.edu

Center for Atmospheric Research

College of Arts and Sciences

RPI Level 0 Data formats

A detailed description of the Level 0 data sets and formats produced by the RPI instrument on the IMAGE satellite

Revision 2.7

April 5, 2000

## Table of Contents

Table of Contents	2

Table of Acronyms	4

List of Tables	5

List of Figures	6

RPI Level 0 Science Data Formats	7

1	RPI Operating Modes, Waveforms, Databin Formats, and ApIDs	7

1.1	Rationale for Data Format Design	7

1.1.1	Databin Types	8

1.2	ApID Assignment	12

1.3	Operating Modes, Waveforms and Databin Formats	12

1.4	Package Structure Design	12

1.4.1	Enumerating databins per frequency	13

1.4.2	Ordering databins per frequency	13

1.4.3	Headers with auxiliary information	15

1.4.4	Filling data section of package	15

2	General Structure of RPI Data Package	15

2.1	CCSDS Preamble	16

2.2	RPI General Header	16

2.3	Preface	16

2.4	Data Header	19

2.4.1	Calculation of nominal frequencies	19

2.4.2	Calculation of total number of frequencies	22

2.5	Frequency Header	23

2.6	Data Section	23

2.7	Checksum	24

3	Calibration and conversion of measured data to physical units	25

3.1	Onboard data processing	25

Analog signal processing	25

3.1.2	Correcting gain and phase differences of X, Y, and Z receiver channels	28

3.1.3	Default and Dynamic calibration	29

3.1.4	Phase and Amplitude calibration	29

3.1.5	Scaling of X and Y channels	29

3.1.6	Despinning of X and Y channels	30

3.1.7	Digital signal processing	30

3.1.8	Linear-to-log signal compression	30

3.2	Converting RPI readings to physical units	31

3.2.1	Converting range bin number to km	32

3.2.2	Converting amplitude to field strength in [ nVp/m ]	32

3.2.3	Converting thermal noise amplitudes to [ dBVrms/root-Hz ]	35

3.2.4	Converting phase data to physical units	36

3.2.5	Converting Doppler bin number to Hz	36

3.2.6	Converting antenna impedance data to physical units	36

RPI Level 0 House Keeping Data Formats	38

4	(R_HK) House Keeping data sets. ApID = 0x02	38

4.1	Housekeeping Header	38

4.2	Miscellaneous status information	39

4.3	Digital Sensor Readings	39

4.4	Analog Sensor Readings	40

4.5	NoGo Table	40

4.6	RPI Power Limits	41

5	(R_SRD) Segment Report data set. ApID=0x04	42

5.1	Segment Data	42

6	(R_MSG) Software Message. ApID=0x06	42

6.1	Software Message	42

7	(R_ECH) Command Echo. ApID=0x08	44

7.1	Command Replica	44

RPI Development Package Formats	45

8	Development Package Formats	45

8.1	ApID=0x1F Frequency Set Response Package	45

8.2	ApID=0x2F Memory Read/Write Response Package	46

8.3	ApID=0x3F VME Read/Write Response Package	46

8.4	ApID=0x4F Digitizer Samples Package	47

Appendix A. Thermal Noise Data Processing	48

A1.	Calculating Log Amplitudes	48

A2.	Calculating Cross Power Terms (XY, XZ and YZ)	49

A3.	Calculating Cross Phases (XY, XZ and YZ)	49

Appendix B. Coupler Band Center Frequency Table	50

Appendix C. Calibration Procedures	51

C1.	Phase calibration procedure	51

C2.	Onboard calibration procedure	52

C3.	Amplitude calibration procedure	53

C3.1.	Input voltage calculation	53

C3.2.	Amplitude calibration coefficients	54

C3.3.	Physical Units table	54

## Table of Acronyms

ApID	:	Application ID (Telemetry Record Type)

BIT	:	Built In Test.

CDF	:	Common Data Format.

CIDP	:	Central Instrument Data Processor

CIT	:	Coherent Integration Time

DBD	:	Double Byte Data

HKD	:	House Keeping Data.

ICD	:	Interface Control Document.

IDFS	:	Instrument Data File Set

LTD	:	Linear Time-domain Data.

LSD	:	Linear Science Data

MET	:	Mission Elapsed Time

PPS	:	Pulses Per Second

PRD	:	Precision Range Data.

RMS 	:	Root Mean Square

RPI 	:	Radio Plasma Imager

SBD	:	Single Byte Data.

S/C	:	Spacecraft

SI		:	Science Instrument.

SMD	:	Spectral Maximum Data.

SPS	:	Staggered Pulse Sequence.

SSD	: 	Standard Science Data.

SST	:	Schedule Start Time.

TN		:	Thermal Noise.

TPC	:	Transmitter Power Card.

TTD	: 	Thermal Time-domain Data.

## List of Tables

Table 1.2-1 	ApID Assignment	12

Table 1.3-1 	Operating Modes, Waveforms and Databin Formats	12

Table 1.4-1 	Number of databins per 1 frequency	13

Table 2.0-1	General Structure of RPI Science Data Package	15

Table 2.1-1 	CCSDS Preamble, Primary Header	16

Table 2.1-2 	CCSDS Preamble, Time Tag	16

Table 2.2-1	RPI General Header	16

Table 2.3-1	Preface	17

Table 2.4-1	Data Header	19

Table 2.5-1	Frequency Header	23

Table 2.7-1	Checksum	24

Table 3.1-1	Nominal receiver voltage gains (X, Y, and Z) for various settings of G, in dB relative to the minimum gain at G=1.	27

Table 3.1-2	Measured receiver voltage gains for various settings of G, in dB relative to the minimum gain at G=1.	27

Table 3.2-1	Physical units for RPI science data	32

Table 3.2-2	Doppler shift frequency	36

Table 3.2-3	Antenna impedance data in physical units	37

Table 4.0-1 	RPI House Keeping data format	38

Table 4.1-1 	HK Header	38

Table 4.2-1 	Miscellaneous status information	39

Table 4.3-1 	Digital sensor readings	39

Table 4.3-2 	Digital Sensor Readings	39

Table 4.4-1 	Analog sensor readings	40

Table 4.5-1 	NoGo Table	41

Table 4.5-2 	Digital and Analog sensor flag parameters	41

Table 4.6-1 	Peak and Average Power Limits	41

Table 5.0-1 	RPI Segment Report data format	42

Table 5.1-1	Segment Data	42

Table 6.0-1 	RPI Segment Report data format	42

Table 6.1-1 	Software message	42

Table 6.1-2 	Message Codes and Parameters	43

Table 7.0-1 	RPI Command Echo format	44

Table 7.1-1 	Command Replica	44

Table 8.1-1	Frequency Set Response package, ApID=0x1F	45

Table 8.2-1	Memory Read/Write Response package, ApID=0x2F	46

Table 8.3-1	VME Read/Write Response package, ApID=0x3F	46

Table 8.4-1	Digitizer Sample package, ApID=0x4F	47

Table C3-1	X/Y Amplitude Corrections and Physical Units table.	55

## List of Figures

Figure 1.1-1 	Linear Time Domain (LTD) databin	8

Figure 1.1-2 	Spectral Science Data (SSD) databin	8

Figure 1.1-3 	Spectral Maximum Data (SMD) databin	9

Figure 1.1-4. 	Precision Group Data (PRD) databin	9

Figure 1.1-5 	Calibration Data (CAL) databin	10

Figure 1.1-6 	Double and Single Byte Data (DBD, SBD) databins	10

Figure 1.1-7 	Thermal-noise Time-domain Data (TTD) databin	11

Figure 2.4-1 	Example of nominal frequency calculations: linear steps, 4 multiplexed frequencies	20

Figure 3.1-2 	Three signal processing channels in RPI.	26

Figure 3.1-3 	Voltage gain of receivers with preamplifiers for gain G = 15.	27

Figure 3.1-4 	Desired effect of amplitude and phase corrections to X and Y output voltages.	28

Figure 3.2-5 	Conversion of amplitudes to physical units.	33

Figure 3.2-6 	Physical units conversion for thermal noise data	35

Figure C1-1 	Phase calibration setup with HP synthesizer	51

Figure C2-1 	Application of calibration signals to X(Y) and Z receiver channels	52

Figure C3-1 	Amplitude calibration setup with HP synthesizer	53

Figure C3-2 	Z channel voltage per digitizer unit, [nV].	54

# RPI Level 0 Science Data Formats

# RPI Operating Modes, Waveforms, Databin Formats, and ApIDs

## Rationale for Data Format Design

RPI is capable of producing data volumes much too high for the telemetry channel throughput. For example, with 5% logarithmic stepping through the nominal frequency band, 128 ranges, 16 repetitions per frequency and 2 polarizations, total data volume collected during a single RPI sounding measurement is

(12 bit in-phase +12 bit quadrature samples) *

3 antennas *

16 Doppler lines *

128 ranges *

2 polarizations

* 142 frequencies = 5,234,688 bytes

With provision of up to 256 Doppler lines, 1024 ranges and smaller frequency steps these volumes may become even larger.

To overcome the problem of high data traffic, a number of measures is devised.

- Onboard Rice Lossless compression performed by CIDP.

- Data thresholding, which can substantially improve compression ratio.

- Logarithmic (lossy) compression. 33% data reduction can be achieved by storing 8 bit logarithmic scale amplitudes and 8 bit phases instead of 12 bit linear scale quadrature components.

- Storing phase differences instead of absolute phases. 16% reduction of spectral data per range bin comes from storing two phase differences relative to the third phase instead of three phases of all three antennas.

- Collapsing of complete spectrum to one Doppler line by selecting the spectrum peak. This is equivalent to considering only one echo per range.

- Collapsing three antennae to one antenna by r.m.s. averaging of amplitudes.

It is not necessary to apply all data reduction measures simultaneously. Only onboard compression of data by CIDP is performed always on all RPI data categories. Data thresholding ratio is specified as a measurement program parameter Z (see RPI Commanding document, Section 1.4.2, Table 1.4-1) which can be optimally adjusted by RPI flight software to control data volume. Logarithmic compression proved to be efficient for storage of spectral domain data (see Section 1.1.1 below), and in this case phase differences are always stored instead of absolute phases. Collapsing spectrum and antenna data are strong measures affecting amount of science information and should be used with caution.

### Databin Types

There is essentially one universal data package format developed for RPI data, which uses different types of a basic measurement unit called a "databin". The databin consists of all measurement data associated with one range/Doppler bin (i.e. log amplitude and phase bytes, or alternately real and imaginary amplitudes for 1 or 3 antennas, Doppler position).

Figure 1.1-1 shows Linear Time Domain (LTD) databin contents. The antenna voltages are sampled twice with 90( phase delay to obtain two 12 bit quadratures per antenna, totaling 9 bytes per databin. The LTD format can be best used for time-domain data (SPS mode, relaxation sounding, chirp sounding).

Figure 1.1-1 	Linear Time Domain (LTD) databin

A more compact Spectral Science Data (SSD) databin (see Figure 1.1-2) is best suited for storing individual lines of Doppler spectrum.

Figure 1.1-2 	Spectral Science Data (SSD) databin

SSD databin can be obtained from the LTD databin by:

- converting the quadratures to a “polar” representation (i.e., amplitude and phase),

- reducing them to 8 bits (logarithmic compression for the amplitude), and

- subtracting phase of antenna Z from the all phases.

Collapsing of complete Doppler spectrum to one line requires storing its Doppler number in the output data bin. Corresponding format 3-Log Polar/8-reduced is shown in Figure 1.1-3.

Figure 1.1-3 	Spectral Maximum Data (SMD) databin

Precision Group Range technique involves sounding on two closely spaced frequencies with reduction of both frequency data to one Doppler line and calculating phase differences with respect to selected phase on the second frequency. The PRD format (Figure 1.1-4) requires storing three amplitudes, five phase differences and one Doppler line.

Figure 1.1-4. 	Precision Group Data (PRD) databin

Figure 1.1-5 shows the databin contents for calibration data, which is very similar to SMD or SSD formats, but stores three amplitudes and three (absolute) phases.

Figure 1.1-5 	Calibration Data (CAL) databin

Another two formats are envisioned to store one antenna data, with r.m.s. average amplitude calculated over three antennas. Double Byte Data (DBD) databin stores 1 byte log scale r.m.s. amplitude and 1 byte Doppler number (Figure 1.1-6). SBD (Single Byte Data) databin further reduces resolution of amplitude and Doppler to fit them in 1 byte.

Figure 1.1-6 	Double and Single Byte Data (DBD, SBD) databins

Finally, a databin format is provided for the Thermal noise Time-domain Data (TTD). In this measurement mode, the following operations are made for each frequency:

- For each antenna, 4(2N)+4 raw quadrature samples are collected. N is the standard RPI parameter used to specify number of transmitted pulses. No transmission is done in the thermal noise mode, and all samples are taken consecutively with 3.2 ms sampling period.

- 2N averaged log amplitudes are computed using 8-point sliding window with 50% overlay.

- For each set of 8 averaged amplitudes (36 raw quadrature samples), three cross-power terms are calculated (corresponding to the antenna pairs XY, XZ, and YZ).

Figure 1.1-7 shows the TTD databin layout.

Figure 1.1-7 	Thermal-noise Time-domain Data (TTD) databin

One TTD databin accommodates:

- eight averaged amplitudes per antenna, totaling 8 x 3 = 24 logarithmic scale amplitudes, and

- one set of the amplitude and phase of the cross-power terms XY, XZ, and YZ.

Total size of one TTD databin is therefore 24+6 = 30 bytes. Minimum 36 samples (N=3) per antenna have to be collected to produce a good data package with a single TTD databin per frequency. Maximum value of N is 8, with 32 TTD databins per frequency.

A detailed description of onboard thermal noise data processing is given in Appendix A.

## ApID Assignment

Each RPI data package is assigned an ApID, which is selected depending on the Databin format as indicated in Table 1.2-1.

Table 1.2-1 	ApID Assignment

| Databin | CAL | DBD | LTD | SMD | SBD | PRD | SSD | TTD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Preface [D] | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| ApID | 0x0C | 0x20 | 0x30 | 0x40 | 0x50 | 0x60 | 0x70 | 0x10 |

There are four types of the science data packages designed to be used during development only. The "development" packages are listed and described in Section 8.

## Operating Modes, Waveforms and Databin Formats

Table 1.3-1 reviews the available choice of RPI scientific data formats, depending on selection of operating mode and waveform.

Table 1.3-1 	Operating Modes, Waveforms and Databin Formats

| Operating Mode | Waveform | Databin Format | L0.5 Data Format | L1 Data Format |
| --- | --- | --- | --- | --- |
| Sounding [O]=S | SPS (X=3) | LTD (D=3) | UDF | CDF Plasmagram |
|  | Chirp (X=2) | DBD (D=2) LTD (D=3) SMD (D=4) SBD (D=5) PRD (D=6) SSD (D=7) |  |  |
|  | Complimentary code (X=1,8,9) |  |  |  |
|  | Long pulse (X=4) |  |  |  |
|  | Short pulse (X=5) |  |  |  |
| Thermal Noise [O]=T | X=0 | TTD (D=8) | UDF | CDF Dynamic Spectrogram |
| Relaxation [O]=R | Short pulse (X=5) | LTD (D=3) | UDF | CDF Plasmagram |
| Whistler [O]=W | 0.5 sec pulse (X=6) | LTD (D=3) | UDF | CDF Plasmagram |
|  | 1.95 sec pulse (X=7) | No output (D=0) | N/A | N/A |
| Calibration [O]=C | Short pulse (X=5) | CAL (D=8) | UDF | N/A |

## Package Structure Design

Arrangement of data into packages imposes two constrains on the data format design:

- Packages of the same ApID must have a fixed size.

- Design should be robust to the loss of some packages during transfer.

A provision must be made to store, for each frequency, the following auxiliary information:

- MET offset from nadir to calculate spin phase

- Frequency offset obtained during search of the quietest frequency

- Autogain selection

- Antenna Impedance data

The size of data collected at a single frequency may vary substantially. In relaxation sounding mode with 8 ranges, 1 polarization, and single byte SBD content total amount of data per frequency is 8 bytes. In a regular sounding with N=5 (32 Doppler lines), 128 ranges, 2 polarizations and 5 byte SSD content the data per frequency amounts to 40,960 bytes. Thus, structuring of data into packages has to account for possible irregular insertion of auxiliary frequency information in the data.

### Enumerating databins per frequency

The data format design suggests enumeration of all databin types (Figures 1.1-1 to 1.1-7) collected at a particular frequency. Table 1.4-1 enlists the expected number of databins in various RPI measurement modes and data formats.

Table 1.4-1 	Number of databins per 1 frequency

| Mode | Waveform | Databin format | Number of databins per 1 frequency |
| --- | --- | --- | --- |
| Sounding [O]=S | SPS [X]=3 | LTD | # of ranges * # polarizations |
|  | Pulse modes [X]=1,4,5,8,9 | LTD | # Doppler lines * # of ranges * # polarizations |
|  |  | SSD |  |
|  |  | SMD | # of ranges * # polarizations |
|  |  | DBD |  |
|  |  | SBD |  |
|  |  | PRD |  |
|  | Chirp [X]=2 | SSD | # Doppler lines * # of ranges * # polarizations |
|  |  | SMD | # of ranges * # polarizations |
|  |  | DBD |  |
|  |  | SBD |  |
|  |  | LTD | # repetitions * # of ranges * # polarizations |
| Relaxation [O]=R | Short pulse [X]=5 | LTD | # of ranges * # polarizations |
| Whistler [O]=W | 0.5 sec pulse [X]=6 |  |  |
| Calibration [O]=C | Short Pulse [X]=5 | CAL | 1 |

### Ordering databins per frequency

The order in which the databins are stored is always:

- Doppler line #1 to N (program parameter N raised to power 2)	(fastest index)

- Range #

- Polarization	(slowest index)

With this arrangement, for any given databin number it is possible to restore its range bin #, polarization and, if used, Doppler line # or repetition #. The following equations for databin number apply:

(1.4-1)

where

= databin number

D 	= total number of Doppler lines,

R 	= total number of ranges (always assumed 1 for TTD databin)

= databin Doppler line

= databin range bin number

= databin polarization

~ means numbering from 0 to n-1 instead of 1 to n.

Restoring of databin parameters is done as follows:

(1.4-2)

(1.4-3)

(1.4-4)

(1.4-5)

Let’s consider the following example:

RPI Sounding, Complimentary Code X=1, SSD databin, 16 Doppler lines, 64 ranges, 2 polarization. Total number of databins per frequency is 16*64*2 = 2048. The databin at Doppler line d = 4 of 16, range r = 8 of 64 and polarization p = 2 of 2 has databin serial number, according to (1.3-1),

(of 2048)

Reverse calculations using (1.3-2 – 1.3-5) give:

(of 2)

115

(of 64)

115 mod 16 + 1= 4 (of 16)

### Headers with auxiliary information

There are two types of headers designed to store complete per-frequency auxiliary information and ensure proper data handling in case of telemetry loss. A Data Header is stored once per package with Frequency reading, MET nadir offset time and databin serial number related to the first databin in the data portion of the package. The Data Header provides information necessary to proceed with data unpacking in case of missing previous telemetry packet. A Frequency Header precedes each numerated sequence of databins, containing autogain and frequency search settings, most probable amplitude, and antenna impedance characteristics. The Frequency Header provides necessary per-frequency information.

Detailed description of the headers can be found in Section 2.

### Filling data section of package

There is no difference in arrangement of the package for different science data other than contents of the databins. The databins are stored in a package one by one in accordance to the order described in section 1.4.2 (Next Doppler line# - next range – next polarization). The length of data section in packages is fixed at 3072 bytes (to meet the requirement to have fixed package lengths for particular ApID). When the end of the defined 3072 byte data section is reached and no more databins can fit the package, the unused part is zero filled. But, if the end of one frequency is reached before the end of the data block is reached, a frequency header is inserted (again, if there is no room for the frequency header at the end of the data block the block is zero filled).  Each new data block contains enough information in the header to identify the first data bin contents, even if the preceding telemetry block is lost.

# General Structure of RPI Data Package

All Scientific Data Formats have identical general structure of the package as indicated in Table 2.0-1. The structure always includes CCSDS Preamble, General Header, Preface, Data Header, Frequency Header, Data Section and Checksum.

Table 2.0-1	General Structure of RPI Science Data Package

|  | RPI Data Block |  |
| --- | --- | --- |
| Sec_2.1 | Sec_2.2 | Sec_2.3 | Sec_2.4 | Sec_2.5 | Sec_2.6 | Sec_2.7 |
| CCSDS Preamble | General Header | Preface | Data Header | Frequency Header | Data Section | Checksum |
| (12 bytes) | (3 bytes) | (103 bytes) | (13 bytes) | (10 bytes) | (3072 bytes) | (1 byte) |

## CCSDS Preamble

The standard CCSDS preamble consists of 6 byte Primary Header and 6 byte Time Tag, as shown in Table 2.1-1 and 2.1-2.

Table 2.1-1 	CCSDS Preamble, Primary Header

| Byte Count No. | Byte Offset No. | Byte Length | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- |
| 0..1 | 0..1 | 2 | 16 bit ApID data: HHHHHiiiiAAAAAAA H- header indicator i – instrument ID A – ApID | N/A | Hex | N/A |
| 2..3 | 2..3 | 2 | Sequence Counter | N/A | Unsigned short | N/A |
| 4..5 | 4..5 | 2 | Byte Count | N/A | Unsigned short | 0-65535 |

Table 2.1-2 	CCSDS Preamble, Time Tag

| Byte Count No. | Byte Offset No. | Byte Length | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- |
| 6..9 | 6..9 | 4 | MET Coarse Time | 100 ms | Unsigned long | 0 to 4294967296 |
| 10..11 | 10..11 | 2 | MET Fine Time | 195.3125 us | Short | 0, 128-65408 |

## RPI General Header

The general header format is standard for all science data packages. The only difference is in the value content of the ApID. The header identifies the data type, the preface length and the software version number.

Table 2.2-1	RPI General Header

| Byte Count No. | Byte Offset No. | Byte Length | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- |
| 12 | 0 | 1 | Application Identification ApID | N/A | int | exact |
| 13 | 1 | 1 | Preface length | N/A | int | 100 |
| 14 | 2 | 1 | Software Version Number | N/A | int | 0-255 |

## Preface

The “Preface” is standard to for all science data. The Preface (Table 2.3-1) contains the data headers that serve to tag the time/satellite characteristics for each measurement as well as list the required parameters to identify the RPI mode of operation. Unless otherwise specified all values are integers. Note: items in the “description” column that are followed by a bracketed abbreviation (e.g. [L]) correspond exactly to measurement parameters specified in the program parameters in the “Measurement Parameter Table” data (see RPI Commanding document, Section 1.4, Table 1.4-1).

Table 2.3-1	Preface

| Byte Count No. | Byte Offset No. | Byte Len | Code | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 15..18 | 0..3 | 4 |  | Mission Elapsed Time of last nadir [MET] Stamp. | 100 millisec | Long | 0 to 4294967296 |
| 19 | 4 | 1 |  | Schedule # | N/A | Byte | 1-32 |
| 20 | 5 | 1 |  | Program # | N/A | Byte | 1-64 |
| 21..22 | 6..7 | 2 | 01 (L) | Lower Frequency Limit | 1kHz | Short | 3kHz-3MHz |
| 23..24 | 8..9 | 2 | 02 (C) | Coarse Frequency If > 0 log steps If < 0 linear steps | 1% 100 Hz | Short | 1-100% 100Hz-1MHz |
| 25..26 | 10..11 | 2 | 03 (U) | Upper Frequency Limit | 1kHz | Short | 3kHz-3MHz |
| 27..28 | 12..13 | 2 | 04 (F) | Fine Frequency Step | 100 Hz | Short | 100Hz-1MHz |
| 29 | 14. | 1 | 05 (S) | No. of fine steps (no zero value) negative value disables multiplexing | Unit | Byte | +1 to +8 -1 to -8 |
| 30..33 | 15..18 | 4 | 06 (X) | Tx Waveform * 0 = no waveform (passive msmt) 1 = Complimentary (51 msec) 2 = FM/CW “Chirp” (125 msec) 3 = Staggered Pulse (786 chips) 4 = Long Pulse (125 msec) 5 = Short Pulse (3.2 msec) 6 = 0.5 sec Pulse 7 = 1.95 sec Pulse 8 = 8 chip complimentary pulse (25 msec) 9 = 4 chip complimentary pulse (13 msec) -1 to –9 same but no phase switching up to four multiplexed waveforms are supported | Table | Four signed bytes | -9 to +9 (no zero value) Each byte contains information on a waveform used in the run |
| 34..37 | 19..22 | 4 | 07 (A) | Tx Antenna options * 1 = Radio Silent (no Tx) 2 = X antenna only 3 = Y antenna only 4 = X+Y in linear polarization 5 = Right Circular Polarization RCP 6 = Left Circular Polarization, LCP 7 = RCP & LCP alternate w.r.t. +Z 8 = X+Y switch linear Pol by 90( -1 to –7 same but bypass antenna coupler | Table | Four signed bytes | -8 to +8 (no zero value) |
| 38..41 | 23..26 | 4 | 08 (N) | No. of Integrated Repetitions * Negative means power integration instead of coherent integration | 2N | Four signed bytes | -8 to +8 |
| 42..45 | 27..30 | 4 | 09 (R) | Pulse Repetition Rate* 0 = 0.5 pps 1 = 1.0 pps 2 = 2.0 pps 3 = 4.0 pps 10 = 10 pps 20 = 20 pps 50 = 50 pps | Table | Four bytes | 0, 1, 2, 4, 10, 20, 50 |
| 46-49 | 31-34 | 4 | 10 (O) | Operating Mode* 0 = Standby 1 = Calibration 2 = Relaxation 3 = Sounding 4 = Thermal Noise 5 = Whistler 6 = Test Pattern | Table | Four bytes | 0 to 5 |
| 50 | 35 | 1 | 11 (W) | Power Limit constraint | Watts | Byte | 0-120 |
| 51 | 36 | 1 | 12 (E) | Start Range 960 km units | 1 Mm | Byte | 0 to 255 |
| 52 | 37 | 1 | 13 (H) | Range Resolution | 10 km | Byte | 24 or 48 |
| 53..54 | 38..39 | 2 | 14 (M) | No. of range bins 8, 16, 32, 64, 128, 256, 512, 1024 | Unit | Byte | 8 to 1024 |
| 55 | 40 | 1 | 15 (G) | Base Gain negative = Fixed Gain positive = Automatic Gain | Table | Byte | -18 to +18 |
| 56 | 41 | 1 | 16 (I) | Frequency Search 0 = Disabled n = 5 freq spaced by n*244 Hz negative = Default calibration positive = Dynamic calibration | Table | Byte | -9 to +9 |
| 57..58 | 42..43 | 2 | 17 (P) | No. of ranges stored 1-1024 | Unit | Short | 1 to 1024 |
| 59 | 44 | 1 | 18 (B) | Bottom of range window | 1 Mm | Byte | 0 to 250Mm |
| 60 | 45 | 1 | 19 (T) | Top of range window | 1 Mm | Byte | 0 to 250Mm |
| 61..64 | 46..49 | 4 | 20 (D) | Databin Format* 0 = No Data 1 = Calibration – CAL 2 = Double Byte Data – DBD 3 = Linear Time Domain – LTD 4 = Spectral Maximum Data –SMD 5 = Single Byte Data – SBD 6 = Precision Range Data – PRD 7 = Spectral Science Data – SSD 8 = Thermal Time Domain – TTD | Table | Four bytes | 0 to 8 |
| 65..68 | 50..53 | 4 | 21 (Z) | Threshold cleaning, in % * 0 = no thresholding | % | Four bytes | 0 to 99 |
| 69-71 | 54-56 | 3 | 22 | Spare program parameter |  |  |  |
| 72 | 57 | 1 |  | High RF Noise setting, 0 = no, 1 = yes. | Unit | Byte | 0 or 1 |
| 73..74 | 58..59 | 2 |  | CIT length | 10 ms | Byte | 0 to 650sec |
| 75 | 60 | 1 |  | Number of multiplexed programs | unit | Byte | 1 |
| 76..77 | 61..62 | 2 |  | Data Status Flags | N/A | Short | N/A |
| 78..81 | 63..66 | 4 |  | Spin Axis Inertial X component | 2s Co. | Int | -1 to +1 |
| 82..85 | 67..70 | 4 |  | Spin Axis Inertial Y component | 2s Co. | Int | -1 to +1 |
| 86..89 | 71..74 | 4 |  | Spin Axis Inertial Z component | 2s Co. | Int | -1 to +1 |
| 90..93 | 75..78 | 4 |  | Spin Phase Angle | Deg. | Int | -180 to 180 |
| 94..97 | 79..82 | 4 |  | Filtered Spin Rate Magnitude | R/Min | Int | +/- 21.4748.. |
| 98.. 101 | 83..86 | 4 |  | MET Coarse @ which Star Tracker is valid | 100 ms | Int | 0 to 4294967296 |
| 102. 105 | 87..90 | 4 |  | MET coarse time of periapse passage | 100 ms | Int | 0 to 4294967296 |
| 106.. 107 | 91..92 | 2 |  | Semi-major axis | 1 km | Short | 0-65535 |
| 108.. 109 | 93..94 | 2 |  | Eccentricity, nominally .4 | LSB= 3*10-5 | Short | 0-1 |
| 110.. 111 | 95..96 | 2 |  | Cosine of angle of inclination | LSB= 3*10-5 | Short | 0-1 |
| 112.. 113 | 97..98 | 2 |  | Argument of Perigee | LSB= 5.5*10-3 | Short | 0-360 |
| 114.. 115 | 99.. 100 | 2 |  | Longitude of the Ascending Node | LSB= 5.5*10-3 | Short | 0-360 |
| 116.. 117 | 101.. 102 | 2 |  | Distance to earth center | 1 km | Short | 0-65535 |

*	indicates up to four parameters may be packed into four bytes. The packing order is reversed, i.e., as byte count increases, the program index decreases from 3 to 0.

## Data Header

The “Data Header” (see Table 2.4-1) contains information necessary to retrieve the databins correctly in case of telemetry losses. See Section 1.4.3 for more details on auxiliary headers design.

Table 2.4-1	Data Header

| Byte Count No. | Byte Offset No. | Byte Length | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- |
| 118..119 | 0..1 | 2 | Frequency step number | unit | Short | 1-65535 |
| 120..121 | 2..3 | 2 | Time offset from nadir MET | 0.1sec | Short | 0 to 6553 sec |
| 122-125 | 4..7 | 4 | Serial number of the first databin in the package, | unit | Long | 0-262143 |
| 126-129 | 8..11 | 4 | Total number of databins per frequency | unit | Long | 8-262144 |
| 130 | 12 | 1 | Multiplexed program number | unit | Byte | 0-3 |

### Calculation of nominal frequencies

RPI selects the actual frequency for transmission by searching for the quietest frequency around the nominal frequency. To obtain the actual sounding frequency,

- the nominal frequency shall be calculated using the Frequency Step Number stored in the Data Header,

- the frequency search adjustment shall be applied using Frequency Search parameter from the Frequency Header.

The Frequency Step Number is converted to the corresponding nominal frequency in kHz using information stored in the Preface. For linear frequency stepping, the nominal frequency is:

(2.4-1)

where

[L] is Lower Frequency Limit from the Preface,

[C] is Coarse Frequency Step (reported negative in this case),

[S]a is the absolute value of Number of Fine Steps,

[F] is Fine Frequency Step, and

is frequency step number from the Data Header.

is the floor function (the largest integer smaller than the argument)

mod  is modulo function (the remainder of integer division).

Example (see Figure 2.4-1):

[L] = 100, [C] = -2000 (i.e., 200 kHz),  [S] = -4, [F] = 250 (i.e., 25 kHz), =15

Figure 2.4-1 	Example of nominal frequency calculations: linear steps, 4 multiplexed frequencies

For logarithmic frequency stepping, the nominal frequency is:

(2.4-2)

where

[L] is Lower Frequency Limit,

[C] is Coarse Frequency Step (in %),

[S]a is the absolute value of Number of Fine Steps,

[F] is Fine Frequency Step, and

is frequency step number from the Data Header.

The [S] Fine Steps are linearly spaced.

Example 1:

[L]=100, [C]=10,  [S]=8, [F]=3, =23

Example 2:

[L]=3, [C]=5,  [S]=1, [F]=don't care, =100

Note that is [C] is a multiple of 3 (3, 6, 9, 12…), the frequency stepping is not "logarithmic", but "coupler band centers" (see explanations below).

For coupler band centers frequency stepping, i.e., when [C] is a positive multiple of 3 (3, 6, 9, 12…) the nominal frequency is taken from a pre-defined table of frequencies. Each of the table frequencies is the center of a coupler band where the maximum efficiency of the tuned transmission is reached. Table of the coupler central frequencies is given in Appendix B.

To convert the frequency index to nominal frequency for the coupler band centers stepping mode, the following procedure shall be used:

- Find the table frequency closest to the Lower Frequency Limit, [L]. (The closest table frequency may appear to be lower or higher than [L].) The found frequency, ft0, will be the first sounding frequency in the measurement, and its index, ,is therefore 0. The index of ft0 in the frequency table will be it0.

- Frequency stepping is then done by incrementing the table index, it, from it0 until the Upper Frequency Limit, [U], is exceeded. The increment to it can be greater than 1 if faster frequency scanning is required. For [C] equal to 3, 6, 9… the increment to the table index is 1, 2, 3…, correspondingly.

Example 1:

[L]=100, [C]=6,  [S]=1, [F]=don’t care, =2

Closest table frequency to 100 kHz is 100.500 kHz, index #65. As [C] equal to 6, the table will be scanned with index increment of 2, i.e., #65 (100.5 kHz), #67 (105.0 kHz), #69 (111.5 kHz), etc. The frequency with =2 is therefore 111.5 kHz.

For fixed frequency measurements (i.e., when [L] is equal to [U]), the nominal frequency is:

(2.4-3)

where

[L] is Lower Frequency Limit,

[S]a is the absolute value of Number of Fine Steps,

[F] is Fine Frequency Step, and

is frequency step number from the Data Header.

i.e., if no frequency multiplexing is requested (i.e., [S] is 1), all frequencies are equal to [L].

### Calculation of total number of frequencies

The total number of frequencies sampled in a single RPI measurement run can be obtained using the following calculations.

For linear frequency stepping, the total number of frequencies is:

(2.4-4)

where

[L] is Lower Frequency Limit,

[U] is Upper Frequency Limit,

[C] is Coarse Frequency Step, and

[S]a is the absolute value of Number of Fine Steps.

For logarithmic frequency stepping, the total number of frequencies is:

(2.4-5)

For coupler band centers frequency stepping, the total number of frequencies is

(2.4-6)

where Ntable is number of the coarse frequency steps, which in this case have to be calculated using Table B-1 (Appendix B) containing coupler band center frequencies:

(2.4-7)

where

[C] is Coarse Frequency Step,

iupper and ilower are indeces of the Upper Frequency Limit, [U] and Lower Frequency Limit, [L], correspondingly, in the coupler frequency table, found by searching the table frequency closest to the nominal frequency.

For fixed frequency measurements, the total number of different frequencies is [S]a, and transmission is repeated [C] times, hence

(2.4-8)

## Frequency Header

The format of Frequency Header is shown in Table 2.5.1. See Section 1.4.3 for more details on auxiliary headers' design.

Table 2.5-1	Frequency Header

| Byte Count No. | Byte Offset No. | Byte Length | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- |
| 131 | 0 | 1 | Gain offset from base gain (4 MSB) Frequency Search (4 LSB) | double steps n*244Hz | Nibble Nibble | 0-3 (0,2,4,6 gain steps) 0 to 4 |
| 132 | 1 | 1 | Most probable amplitude | TBD | Byte | TBD |
| 133 | 2 | 1 | Current on X antenna [Ix] | 10mamp | Byte | 0-2.55 amp |
| 134 | 3 | 1 | Voltage on +X dipole antenna [Vx1] | 10 volt | Byte | 0-2550 Volt |
| 135 | 4 | 1 | Voltage on -X dipole antenna [Vx2] | 10 volt | Byte | 0-2550 Volt |
| 136 | 5 | 1 | Current on Y antenna [Iy] | 10mamp | Byte | 0-2.55 amp |
| 137 | 6 | 1 | Voltage on +Y dipole antenna [Vy1] | 10 volt | Byte | 0-2550 Volt |
| 138 | 7 | 1 | Voltage on -Y dipole antenna [Vy2] | 10 volt | Byte | 0-2550 Volt |
| 139-140 | 8-9 | 2 | First Range Bin | Units | Short | 0-511 |

Storing Frequency Header in each data package is excessive if more that one package is required to hold one frequency data, but this measure provides necessary robustness of data format to telemetry data losses.

## Data Section

Data Section contains an array of databins arranged in the sequential order as described in Section 1.4.1 and 1.4.2, possibly with frequency headers. The length of the Data Section is fixed at 3072 bytes.

The Data section can hold more than one frequency data and therefore store Frequency Headers (see Section 2.5 for format description) which separate individual frequency data. One Frequency Header is placed in front of every databin sequence, unless the Data Section begins with the first databin of the frequency and therefore the Frequency Header preceding the Data Section (see Section 2.5) can be used.

The actual frequency setting is not stored in the Frequency Header. To calculate actual frequency of nth frequency data in the package, the frequency step number has to be obtained first by adding the frequency step number from the Data Header (see Section 2.4) to n. Then, formulas (2.4-1) or (2.4-2) shall be used to obtain the nominal frequency. Finally, the actual frequency is obtained by applying frequency search correction to the nominal frequency:

(2.6-1)

where FS is frequency search adjustment value from the Frequency Header, and [I] is Frequency Search parameter from the Preface.

## Checksum

This section contains 1 byte checksum calculated from byte 7 to end of package by successively applying Exclusive-Or operation on the bytes of the package.

Table 2.7-1	Checksum

| Byte Count No. | Byte Offset No. | Byte Length | Description | Units | Type | Range |
| --- | --- | --- | --- | --- | --- | --- |
| N-1 | 0 | 1 | Checksum | N/A | Byte | 0-255 |

# Calibration and conversion of measured data to physical units

## Onboard data processing

Figure 3.1-1 shows a complete diagram of RPI onboard data processing, further detailed in subsequent sections of Chapter 3. For illustration purpose, the diagram indicates an assumed signal of 100 nVp/m in the x, y, and z directions undergoing SSD processing with a gain [G] = 15 and operation at a frequency of 65 kHz. To simplify the example, the phase differences of the receivers are not reflected in the processing. The signal phase is assumed 0( so that the in-phase component I is equal to the signal amplitude, and the quadrature component Q is zero.

### Analog signal processing

Figure 3.1-2 shows the diagram of analog signal processing circuitry of RPI.

Figure 3.1-2 	Three signal processing channels in RPI.

As Figure 3.1-2 indicates, there are two equal channels, X and Y, each connected to a 500 m dipole antenna. Channel Z is provided with a shorter, 20 m antenna, and therefore has to compensate for the smaller input signal by yielding a higher voltage gain. The  broadband preamplifiers in the Z channel have 4 dB more gain than the X/Y preamplifiers, and the Z receiver has ~10 dB more gain. This results in a ~14 dB higher gain in Z channel, unless the high gain setting is selected in the Z preamp. In the latter case, the Z channel has ~26 dB more gain.

All receivers have selectable gain that can be set fixed or chosen optimally in the autogain mode. X and Y gain setting are always set identical, the Z gain is typically greater because of the shorter Z antenna. There are 18 different combinations of two gains (Z and X/Y) that are encoded in a single value of the nominal gain, [G], as shown in Table 3.1-1. The actual gain readings (in dB above the minimum receiver gain) are provided in Table 3.1-2 for the X, Y, and Z channels. The minimum receiver gain is frequency dependent for all receiver channels, and can be derived from the calibration results as discussed below.

Table 3.1-1	Nominal receiver voltage gains (X, Y, and Z) for various settings of G, in dB relative to the minimum gain at G=1.

| G | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| dB steps | 0 | +6 | +12 | +18 | +24 | +30 | +24 | +30 | +36 | +42 | +48 | +54 | +24 | +30 | +36 | +42 | +48 | +54 |
| Z preamp | low | low | low | low | low | low | hi | hi | hi | hi | hi | hi | low | low | low | low | low | low |

Table 3.1-2	Measured receiver voltage gains for various settings of G, in dB relative to the minimum gain at G=1.

| G | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| X | 0 | 4.6 | 10.9 | 18 | 24.3 | 30.7 | 24.3 | 30.7 | 37.1 | 42.7 | 49.1 | 55.5 | 24.3 | 30.7 | 37.1 | 42.7 | 49.1 | 55.5 |
| Y | 0 | 3.8 | 10.9 | 20.6 | 24.4 | 32.1 | 24.4 | 32.1 | 37.1 | 47.3 | 55. | 60. | 24.4 | 32.1 | 37.1 | 47.3 | 55. | 60. |
| Z | 0 | 5.2 | 9.3 | 20.3 | 23.5 | 29.2 | 35.5 | 40.6 | 46.7 | 56.8 | 61.9 | 68. | 23.5 | 28.6 | 34.7 | 44.8 | 49.9 | 56. |

Figure 3.1-3 	Voltage gain of receivers with preamplifiers for gain G = 15.

Figure 3.1-3 shows the actual voltage gains in dB of the X, Y, and Z receivers for the gain setting of 15

(3.1-1)

where Vout(f) is receiver output voltage before the digitizer, and Vin(f) is input voltage at the antenna terminals. Using the actual gains for G=15 and the table of measured gains relative to the minimum gain (Table 3.1-2), it is possible to calculate the gains for all frequencies and base gain settings.

### Correcting gain and phase differences of X, Y, and Z receiver channels

RPI measures the 3 orthogonal components of electric field vectors and derives angle-of-arrival of the echoes reflected from magnetospheric plasma. The signals from each antenna go through individual receiver channels that introduce frequency-dependent amplification and phase shifts. Differences between the channel characteristics would introduce errors to angle-of-arrival calculations, unless corrected. Therefore, calibration of the phase and gain characteristics of the receiver channels assumes vital importance to the angle-of-arrival data validity.

To ensure proper compensation of differences between the receiving channels, RPI introduces phase and amplitude corrections, for each sounding frequency, to the quadrature components measured by the X and Y receivers. Channel Z acts as the amplitude and phase reference and therefore is passed through unchanged. The purpose of introducing the corrections is to obtain identical response of all channels to the input signal. Figure 3.1-4 illustrates the correction process, assuming identical field strengths along the x, y, and z directions.

Figure 3.1-4 	Desired effect of amplitude and phase corrections to X and Y output voltages.

The correction applied to the X and Y channels makes the outputs identical. The actual correction factors are calculated based on measurements of the voltage gain and phase shifts of the receiver channels.

### Default and Dynamic calibration

Two calibration modes are implemented

- "DEFAULT". A CAL Table is stored in the flight software with results of the X, Y, Z channel calibrations obtained in the laboratory (see description of the phase calibration procedure in Appendix C). The key disadvantage of the "default" correction algorithm is its inability to reflect the actual variability of the RPI hardware characteristics with temperature, time, mechanical impacts, etc. during the mission. Also, the CAL Table contains data collected for a particular, predefined set of frequencies, and therefore when the actual sounding frequency does not match any of the frequencies in the default CAL Table, the algorithm has to select the closest available frequency instead.

- "DYNAMIC": RPI has calibration circuitry that allows the attenuated transmitter signal to go through the receiver channels. The measured receiver response can be directly used to compensate for the inequalities. The dynamic calibration senses the actual receiver characteristics for each sounding frequency immediately before the transmission starts. However, the calibration signals for the X/Y channels are affected by the impedance characteristics of the antennas and therefore the calibration voltages applied at the receiver inputs vary with frequency. A loopback laboratory calibration was conducted to measure the amplitude and phase of the calibration source signal. Further description of the loopback calibration is given in Appendix C.

Either "default" or "dynamic" calibration can be selected in the RPI measurement programs. When dynamic calibration is chosen, it must be combined with the frequency search procedure as both of them are performed during the period of time allocated for the frequency search. Calibration data, regardless of their origin, are reported into the telemetry channel in a data package with ApID = 0x0C. The unified data format (see Section 2) is used to hold calibration data; however, there are no frequency headers in the Data Section of the CAL packets (see section 2.6).

### Phase and Amplitude calibration

Gain and phase characteristics of the analog circuitry were studied in laboratory conditions, as described in detail in Appendix C.

### Scaling of X and Y channels

For low Z preamp gain, the Z axis channel has ~14 dB more gain than X and Y, but the output signals from the X and Y channels will typically be larger due to the different  antenna lengths. An appropriate scaling is required to optimally package all data for telemetry and avoid data storage related saturation of the X and Y readings. The scaling factor of 1/8 is introduced for the X and Y channel data, which has to be removed during ground data processing to return to the case of matched X, Y, Z channels.

### Despinning of X and Y channels

After the differences in X and Y channels are removed by calibration, it becomes possible to compensate for the spinning of the X and Y antennas (nominally at 1/2 rpm). The despinning procedure calculates the projection of the E-field vector in the x', y', z' system, where

- the x' axis points to the center of the Earth,

- the z' axis, equal to the z axis, points in the direction of the orbital angular momentum, and

- the y' axis is perpendicular to the x' axis in the orbital plane.

The IMAGE spin vector points opposite to the z axis, and therefore the voltages in the primed coordinate system are

(3.1-2)

Here Vx, Vy, Vz are the corrected voltages in the antenna coordinate system, S is the spin rate ( S = 1/120 sec), and t' is the time measured from the last alignment of the x axis with the x' axis.

### Digital signal processing

Certain RPI waveforms require specialized onboard signal processing. The processing includes pulse compression for the complementary phase code sequences, and spectral analysis for equidistant pulse sequences. For the purpose of calibration and conversion of amplitudes to physical units, it is important that the "digital" gain of the signal processing is known.

### Linear-to-log signal compression

In order to reduce the telemetry data volume, some of the output data are converted to amplitude/phase representation and logarithmically compressed. The amplitude Alin and phase  can be obtained from the in-phase and quadrature samples I and Q using equation (3.1-3):

(3.1-3)

The phase ( is then stored in an 8-bit integer, in linear 360º/255 steps. The amplitude Alin is converted to the logarithmic scale and stored in another 8-bit integer:

(3.1-4)

The constants C1 and C2 are selected to accommodate the dynamic range of Alin in the 256 levels of Alog. The choice of C1 and C2 is influenced by the need to minimize real-time computations. By rewriting (3.1-4) as

(3.1-5)

the root function does not have to be calculated. Also, log2() function can be used instead of a slower implementation of log10():

(3.1-6)

C1 shall be then selected to allow enough dynamic range. The 12-bit digitizer produces 12 bit numerical voltage values (11 bits and sign) for I and Q. Assuming that both I and Q are saturated, the maximum Alin is (211-1) · √2. For 4, 8, and 16 chip phase code waveforms, the pulse compression processing (Section 3.1.7) increases the maximum amplitude 4, 8, and 16 times, correspondingly, resulting in (213-1) · √2, (214-1) · √2, and (215-1) · √2 values of the maximum Alin. Therefore, the maximum amplitude to be ever converted to log scale is 32767 · √2 = 46340 = 93.32 dB. Making

(3.1-7)

allows for 255 · 3.0103/8 ≈  96 dB dynamic range of Alog and a convenient formula for Alog calculation:

(3.1-8)

To simplify the ground processing, C2 is selected to always reference the maximum possible value of Alin, for each waveform, to the maximum level of Alog (i.e., 255):

(3.1-9)

Shifting of the reference level by introducing the waveform-dependent C4 constant normalizes the DSP gain from the pulse compression (Section 3.1.7) and thus simplifies the log-to-linear decompression algorithm discussed below in the Section 3.2.2.1.

## Converting RPI readings to physical units

Table 3.2-1 shows the choice of physical units for the RPI science data.

Table 3.2-1	Physical units for RPI science data

| Measured parameter | Standard units | Stored in the data as | Calibration/Conversion |
| --- | --- | --- | --- |
| Nominal Frequency | KHz | Frequency Step Number | Section 2.4.1 |
| Range | Km | Range Bin Number | Section 3.2.1 |
| Field Strength | nVp/m( | 12 bit quadrature component | Section 3.2.2 |
| Field Strength | nVp/m* | 8 bit log amplitude, except TTD databin | Section 3.2.2 |
| Voltage | dBV/root-Hz | 8 bit log amplitude (TTD databin) | Section 3.2.3 |
| Antenna voltage | Vrms | 8 bit values in Frequency Header | Section 3.2.6 |
| Antenna current | MA | 8 bit values in Frequency Header | Section 3.2.6 |
| Phase | Degrees | 8 bit linear phase | Section 3.2.4 |
| Doppler Frequency | Hz | Doppler Bin Number | Section 3.2.5 |

### Converting range bin number to km

The range bin number,  for a particular databin is obtained using Equation 1.4-4, Section 1.4.2. Then the range in km is

(3.2-1)

where

[E]	is Start Range in 960 km units (from Preface)

is range bin number

rst	is First Range Bin (from Frequency Header, Table 2.5-1)

[H]	is Range Resolution in 10 km (from Preface), i.e., 24 or 48

### Converting amplitude to field strength in [ nVp/m ]

Figure 3.2-1 details the ground processing steps to convert measured amplitudes from the raw telemetry representation to the field strengths in [ nVp/m ]. Given example values continue from Figure 3.1-1.

Onboard calibration tables used by the flight software v31 and below have to be replaced by an updated calibration data now available. Before the calibration corrections to the quadrature samples can be removed, un-despinning of the data has to be done. After the new corrections are introduced, despinning has to be reapplied.

#### Log-to-linear decompression

RPI science data with databin formats SSD, SMD, PRD, SBD and DBD (see Section 1.1.1) report 8 bit logarithmically compressed amplitudes. The amplitudes have to be converted back to linear scale before they enter the rest of the conversion process:

(3.2-2)

where Alog is the stored amplitude, and C1 and C3 are the compression algorithm constants:

(3.2-3)

Figure 3.2-5 	Conversion of amplitudes to physical units.

#### Polar to Rectangular Conversion

For spectral domain data, the in-phase and quadrature components are restored from the amplitude and phase:

(3.2-4)

where ( is the phase in radians obtained from the 8-bit stored value as discussed below in Section 3.2.4.

#### Un-despinning

The de-spinning procedure (Section 3.1.6) has to be undone before the v28 corrections  can be removed. The rotation is done in the opposite direction to de-spinning (3.1-2):

(3.2-5)

Vx and Vy are the voltages in the antenna coordinate system, S is the spin rate  (1/120 sec), and t' is the time measured from the last alignment of the x axis with the x' axis. For all time domain data, t' is the time offset from the nadir, (Tnadir(f), stored in Data Header of each telemetry packet. If more than one frequency data fits one packet, (Tnadir(f) for the second, third,… frequency of the packet has to be interpolated (or extrapolated, for the last packet). For the spectral domain data, 0.5 CIT has to be added to t' (see Section 3.2.5 for CIT calculation). Spin rate magnitude S is stored in the Preface.

#### Un-scaling

All X and Y channel data had been scaled down by a factor of 8 for the purpose of optimal binary data storage (see Section 3.1.5). This factor has to be removed here by multiplying the amplitudes by 8.

#### Removing correction factors

Only amplitude corrections for the flight software v31 and below have to be removed, so the un-calibration procedure is simply:

(3.2-6)

where Axc and Ayc are the amplitude corrections introduced by the flight software. The onboard correction factors are reported in the calibration packet as 8-bit log-scale amplitudes and 8-bit phases for the channels X, Y, and Z. Axc and Ayc can be restored from CAL packet data using the following formula:

(3.2-7)

where CALx and CALy are the calibration amplitudes of X and Y channels.

#### Re-calibrating

Re-calibration involves amplitude scaling only, and therefore can be expressed simply as

(3.2-8)

The table with the new amplitude correction factors and  can be found in Appendix C, Table C1-1.

#### Despinning

The de-spinning procedure (Section 3.1.6) has to be done after the new corrections are applied, using the equations (3.1-2) and the offset time t' from Section 3.2.2.3.

#### Applying coefficients from the Physical Units Table

The Physical Units Table Each table has coefficients Cx,y,z( f, [G] ) in [nV/unit] for all settings of base gain [G] and selected set of frequencies. The table is derived from the Z channel calibration results obtained during the amplitude calibration at [G] = 15 (see description of the calibration in Appendix C and the coefficient values in Table C3-1). The coefficients for other settings of [G] are obtained using the relative gain data shown in Table 3.1-2:

(3.2-9)

#### Calculations of field strength

The received field strength, ER, is proportional to the antenna voltage, V:

(3.2-10)

where the proportionality factor L' is the effective antenna length, L' ( 0.5La, La is the tip-to-tip dipole length. The effective antenna lengths are

(3.2-11)

### Converting thermal noise amplitudes to [ dBVrms/root-Hz ]

The processing steps to convert thermal noise amplitudes from the raw telemetry representation to [ dBV(rms)/root-Hz ] are shown in Figure 3.2.2.

Figure 3.2-6 	Physical units conversion for thermal noise data

Logarithmic compression of TTD amplitudes is done differently from the spectral domain data (see Appendix A). To convert TTD amplitudes to the linear scale, the following formula is used:

(3.2-12)

Un-scaling, un-calibrating, re-calibrating and conversion to nVp is done the same way it is done for other databins. Then nVp are converted to Vrms, and then the thermal noise energy collected over the receiver bandwidth of 300 Hz is normalized to 1 Hz, which corresponds to 1/(300 factor in voltage. Finally, the value is put in dB scale.

### Converting phase data to physical units

All phase values given in the RPI data can be converted from 8 bit integer number to 1( units by multiplying them with 360/255.

### Converting Doppler bin number to Hz

The coherent integration time is

, [s]	(3.2-13)

[N]a	is absolute value of Number of Repetitions

[S]' 	is the Number of Fine Steps, [S], only if it is a positive value, 1 otherwise

[R]'	is Pulse Repetition Rate in pps units; 	when [R] from Preface is 0, [R]' is 0.5

The Doppler frequency increments are

,  [Hz]	(3.2-14)

The Doppler frequencies corresponding to the Doppler bin numbers are listed in Table 4.4-1.

Table 3.2-2	Doppler shift frequency

| [N] | Doppler bin numbers | Doppler frequencies, Hz |
| --- | --- | --- |
| 0 | 1 | N/A |
| 1 | 1-2 | -1/2(d, +1/2(d |
| 2 | 1-4 | -3/2(d, -1/2(d, +1/2(d, +3/2(d |
| 3 | 1-8 | -7/2(d, -5/2(d, …,-1/2(d, +1/2(d,…+5/2(d, +7/2(d |
| 4 | 1-16 | -15/2(d, -13/2(d, …,-1/2(d, +1/2(d,…+13/2(d, +15/2(d |
| 5 | 1-32 | -31/2(d, -29/2(d, …,-1/2(d, +1/2(d,…+29/2(d, +31/2(d |
| 6 | 1-64 | -63/2(d, -61/2(d, …,-1/2(d, +1/2(d,…+61/2(d, +63/2(d |
| 7 | 1-128 | -127/2(d, -125/2(d, …,-1/2(d, +1/2(d,…+125/2(d, +127/2(d |

### Converting antenna impedance data to physical units

Frequency Header contains six 8-bit values from the antenna impedance measurement:

Table 3.2-3	Antenna impedance data in physical units

| Measured characteristic | Physical Units | Conversion Polynomial |
| --- | --- | --- |
| Current on X antenna [Ix] | mA | 0.017196*x2+23.697063*x+18.055805 |
| Voltage on +X dipole antenna [Vx1] | V(r.m.s) | 0.001041*x3-0.079089*x2+ 6.833423*x+77.628601 |
| Voltage on -X dipole antenna [Vx2] | V(r.m.s) | 0.000340*x3-0.072471*x2+10.139749*x+27.581501 |
| Current on Y antenna [Iy] | mA | 0.021766*x2+21.881399*x+15.814330 |
| Voltage on +Y dipole antenna [Vy1] | V(r.m.s) | 0.041969*x2+3.503154*x+96.108014 |
| Voltage on =Y dipole antenna [Vy2] | V(r.m.s) | 0.039404*x2+3.459442*x+96.996135 |

# RPI Level 0 House Keeping Data Formats

The following sections introduce and describe the formats for housekeeping (HK) data produced by the RPI instrument, which include R_HK Housekeeping package with Build-In Test results, R_SRD Segment Report package containing the contents of RPI SRAM segments, R_MSG Software Message package containing software generated message, and R_ECH Command Echo package with a copy of the latest ground command.

# (R_HK) House Keeping data sets. ApID = 0x02

The RPI house keeping represents the RPI health and safety data package. The R_HK package is generated by RPI to report on system (hardware and software) status. The package is sent periodically (nominally every 10 minutes) or by request from the ground. The structure of the data block is given in sections 5.1 to 5.6. Each section describes part of the data block that is given by the overview in Table 5.0-1.

Table 4.0-1 	RPI House Keeping data format

|  | R_HK Block |  |
| --- | --- | --- |
| Sec_2.1 | Sec_5.1 | Sec_5.2 | Sec_5.3 | Sec_5.4 | Sec_5.5 | Sec_5.6 | Sec_2.5 |
| Data Package Preamble | HK Header | Misc. status info | Digital Sensors | Analog Sensors | NoGo Table | Power Limits | Checksum |

## Housekeeping Header

Housekeeping Header format is identical to all four HK packages (R_HK, R_SRD, R_MSG, and R_ECH). It contains five items, as shown in Table 5.1-1.

Table 4.1-1 	HK Header

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 7 | 0 | 1 | Package ApID | N/A | N/A |
| 8 | 1 | 1 | Software version | N/A | 0-255 |
| 9..12 | 2..5 | 4 | CIDP MET stamp | 0.1 sec | 0 to 4294967296 |
| 13..16 | 6..9 | 4 | RPI MET stamp | 0.1 sec | 0 to 4294967296 |
| 17..18 | 10..11 | 2 | Argument of perigee | LSB=5.5*10-3 | 0 to 360 |

Package ApID is preserved for data identification purpose outside the standard data archive environment. Software version is reported for backward compatibility in case of design changes. CIDP and RPI time stamps are given for the clock comparison purpose. Orbital position phase is given to verify calculation algorithm.

## Miscellaneous status information

This section contains various status information items listed in Table 5.2-1.

Table 4.2-1 	Miscellaneous status information

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 19..22 | 0 | 4 | Last SST in the SST Queue | 0.1 sec | 0 to 4294967296 |
| 23 | 4 | 1 | Memory checksum failure | N/A | 0..1, 1 -failed |
| 24 | 5 | 1 | Program status (format variable) | N/A | 0-255 |
| 25 | 6 | 1 | Communication Status (from serial port UART) | N/A | 0-255 |

## Digital Sensor Readings

This section contains digital sensor readings in accordance with the state of digital I/O lines on the BIT card.

Table 4.3-1 	Digital sensor readings

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 26 | 0 | 1 | Digital sensor readings | N/A | 0-255 |

Each bit of the status byte signifies if reading is valid or not valid. The actual bit readings need to be compared against the expected "Go" value to correctly interpret the result. This comparison is done onboard to fill the NoGo Table where 1 always indicates "NoGo" (and 0 indicates "Go").

The Digital Sensors names and "Go" condition are listed in Table 5.3-2. The following categories of signals are monitored:

- 16MHz	RPI master 16 MHz oscillator signal

- Vc	Antenna coupler voltages +12 and +24V

- V	DC -5, -15 and +15V

Table 4.3-2 	Digital Sensor Readings

|  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Signal name | - | 16 MHz | +24 Vc | - | +12Vc | -5V | -15 V | +15 V |
| GO condition | - | 1 | 1 | - | 1 | 0 | 0 | 1 |

Go conditions for digital sensors are specified in the onboard ARMENU control structure, question 351 (see RPI Commanding document, Section 2).

## Analog Sensor Readings

This section contains the measurements from the analog input channels on the BIT card. The values are 16 bit integers with 12 bits containing raw value from the ADC.

Table 4.4-1 	Analog sensor readings

| Byte Count Offset | Byte Offset No | Byte Length | Description | Type | Units | Range |
| --- | --- | --- | --- | --- | --- | --- |
| 27..28 | 0..1 | 2 | Channel.00 Xmtr Xb | B | 5/4096 V | 0-2.5 V |
| 29..30 | 2..3 | 2 | Channel.01 Xmtr Yb | B | 5/4096 V | 0-2.5 V |
| 31..32 | 4..5 | 2 | Channel.02 1st Lob | B | 5/4096 V | 0-2.5 V |
| 33..34 | 6..7 | 2 | Channel.03 SysTemp | S | 5/4096 V | 0-2.5 V |
| 35..36 | 8..9 | 2 | Channel.04 500 kb | B | 5/4096 V | 0-2.5 V |
| 37..38 | 10..11 | 2 | Channel.05 3.84 Mb | S | 5/4096 V | 0-2.5 V |
| 39..40 | 12..13 | 2 | Channel.06 95 kb | S | 5/4096 V | 0-2.5 V |
| 41..42 | 14..15 | 2 | Channel.07 X+Tmp | B | 5/4096 V | 0-2.5 V |
| 43..44 | 16..17 | 2 | Channel.08 X-Tmp | B | 5/4096 V | 0-2.5 V |
| 45..46 | 18..19 | 2 | Channel.09 Y+Tmp | S | 5/4096 V | 0-2.5 V |
| 47..48 | 20..21 | 2 | Channel.10 Y-Tmp | S | 5/4096 V | 0-2.5 V |
| 49..50 | 22..23 | 2 | Channel.11 Ztmp | S | 5/4096 V | 0-2.5 V |
| 51..52 | 24..25 | 2 | Channel.12 RFX+ | B | 5/4096 V | 0-2.5 V |
| 53..54 | 26..27 | 2 | Channel.13 RFX- | B | 5/4096 V | 0-2.5 V |
| 55..56 | 28..29 | 2 | Channel.14 RFY+ | B | 5/4096 V | 0-2.5 V |
| 57..58 | 30..31 | 2 | Channel.15 RFY- | B | 5/4096 V | 0-2.5 V |
| 59..60 | 32..33 | 2 | Channel.16 RFSmpZ | B | 5/4096 V | 0-2.5 V |
| 61..62 | 34..35 | 2 | Channel.17 RFSmpX | B | 5/4096 V | 0-2.5 V |
| 63..64 | 36..37 | 2 | Channel.18 IFSmpZ | B | 5/4096 V | 0-2.5 V |
| 65..66 | 38..39 | 2 | Channel.19 IFSmpY | B | 5/4096 V | 0-2.5 V |
| 67..68 | 40..41 | 2 | Channel.20 2500 b | S | 5/4096 V | 0-2.5 V |
| 69..70 | 42..43 | 2 | Channel.21 400 kb | S | 5/4096 V | 0-2.5 V |
| 71..72 | 44..45 | 2 | Channel.22 XvarI | B | 5/4096 V | 0-2.5 V |
| 73..74 | 46..47 | 2 | Channel.23 YvarI | B | 5/4096 V | 0-2.5 V |
| 75..76 | 48..49 | 2 | Channel.24 YvarV | B | 5/4096 V | 0-2.5 V |

Type B 	= 	Burst measurement of a pulse signal must be done during sounding only.

Type S 	= 	Single measurement of a continuous signal may be done anytime.

## NoGo Table

This section contains 5 bytes indicating Go/NoGo condition of all sensor readings.  Each bit of the NoGo Table bytes is set to 1 (NoGo) if:

- analog sensor reading is outside the onboard red tolerance limits or digital sensor reading is not GO (see Table 5.2-2), and

- the sensor is specified as capable of generating NoGo condition.

Onboard red limits are specified in questions 330-343 of the ARMENU control structure (see RPI Commanding document, section 2.1), GO conditions of digital sensors are given in question 351 of the ARMENU structure, and sensors capable of generating NoGo condition are listed in questions 361-365.

Table 4.5-1 	NoGo Table

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 77 | 0 | 1 | Digital Sensor | N/A | 0-255 |
| 78 | 1 | 1 | Analog Status : Ch00-Ch07 | N/A | 0-255 |
| 79 | 2 | 1 | Analog Status : Ch08-Ch15 | N/A | 0-255 |
| 80 | 3 | 1 | Analog Status : Ch16-Ch23 | N/A | 0-255 |
| 81 | 4 | 1 | Analog Ch24 and Reserved Bits | N/A | 0-255 |

The Digital and Analog sensor flags and their associated reading parameters are listed in Table 5.5-2.

Table 4.5-2 	Digital and Analog sensor flag parameters

| Line Count | Category | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Byte 1 digital | - | 16 MHz | +24 Vc | - | +12Vc | -5V | -15 V | +15 V |
| 4 | Ch00-Ch07 analog. | XMTR 1 | XMTR 2 | 1st LO | SysTemp | C140K | 3.84MHz | 95kHz | X+tmp |
| 5 | Ch08-Ch15 analog. | X-tmp | Y+tmp | Y-tmp | Ztmp | RFX+ | RFX- | RFY+ | RFY- |
| 6 | Ch16-Ch23 analog. | RFSmpZ | RFSmpX | IFSmpZ | IFSmpX | 2500 Hz | 400 kHz | XvarI | YvarI |
| 7 | Reserved | XyvarV | Reserved |

## RPI Power Limits

If necessary, PRI can be instructed to use power limit different from the limit specified in the measurement programs (see program parameter 11(W) in the Preface, Section 2.3). There is a pass-through command R_SYS_PLIM_SET that specifies Peak and Average power limits. Before running a program, RPI evaluates all available limits, and selects the minimum.

The following section of HK package reports current settings of peak and average power limits as instructed from the ground.

Table 4.6-1 	Peak and Average Power Limits

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 82 | 0 | 1 | Peak Power Limit | Watts | 0-255 |
| 83 | 1 | 1 | Average Power Limit | Watts | 0-255 |

# (R_SRD) Segment Report data set. ApID=0x04

This report segment is generated by RPI in response to the ground request R_MEM_DATA_SEND, which instructs RPI to downlink a specific segment of memory from the RPI CPU. The segment can be a section of the flight software or one of the control data structures (Programs, Schedules, SST Tables, ARMENU). The structure of the Segment Report package is given in Table 6.0-1.

Table 5.0-1 	RPI Segment Report data format

|  | RPI-SRD Block |  |
| --- | --- | --- |
| Sec_2.1 | Sec_5.1 | Sec_6.1 | Sec_2.4 |
| Data Package Preamble | HK Header | Segment data | Checksum |

## Segment Data

The segment data are stored in accordance to the format described in Table 6.1-1.

Table 5.1-1	Segment Data

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 19..20 | 0..1 | 2 | SCLen Segment length | N/A | 0-65536 |
| 21..24 | 2..5 | 4 | Segment Address | 32 bit words | 0-0x00FFFFFF |
| 25..SCLen*4+25 | 3..SCLen*4+3 | SCLen*4 | Segment Contents | N/A | N/A |

# (R_MSG) Software Message. ApID=0x06

When a software fault is detected, a R_MSG software message package is generated. The message contains a message code (associated with a table for identification of the problem type), and two message parameters. The structure of the Software Message package is given in Table 7.0-1.

Table 6.0-1 	RPI Segment Report data format

|  | RPI-MSG Block |  |
| --- | --- | --- |
| Sec_2.1 | Sec_5.1 | Sec_7.1 | Sec_2.4 |
| Data Package Preamble | HK Header | Software message | Checksum |

## Software Message

Table 6.1-1 	Software message

| Byte Count Offset | Byte Offset | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 19 | 0 | 1 | Message Code | Table 7.1-2 | 0-255 |
| 20..23 | 1..4 | 4 | Message Parameter #1 | Table 7.1-2 | Message dependent |
| 24..27 | 5..8 | 4 | Message Parameter #2 | Table 7.1-2 | Message dependent |

Message codes and the associated parameters are listed in Table 7.1-2.

Table 6.1-2 	Message Codes and Parameters

| Message Code | Message Code Description | Message Parameters Description |
| --- | --- | --- |
| 202 | 0xCA | CIT start timeout | #1 -- Timeout, sec |
| 203 | 0xCB | Pulse start timeout | #1 -- Timeout, sec |
| 204 | 0xCC | Prerun condition timeout | #1 -- Timeout, sec |
| 205 | 0xCD | Blank command parameter | #1 -- Command stem |
| 207 | 0xCF | No timing port signal |  |
| 208 | 0xD0 | No 1_PPS signal |  |
| 209 | 0xD1 | No Clock Pulse signal |  |
| 210 | 0xD2 | Digitizer timeout | #1 -- Timeout, sec |
| 211 | 0xD3 | EEPROM load error |  |
| 212 | 0xD4 | EEPROM save error | #1 -- Address, 32 bit |
| 213 | 0xD5 | Data upload checksum error | #1 -- Checksum, 8 bit |
| 214 | 0xD6 | Bad command stem | #1 -- Command stem |
| 215 | 0xD7 | System is not in HiPower to execute command |  |
| 216 | 0xD8 | Communications: Unknown Error |  |
| 217 | 0xD9 | Communications: Framing Error |  |
| 218 | 0xDA | Communications: Sync. Byte Error |  |
| 219 | 0xDB | Communications: Bad Command Message Checksum |  |
| 220 | 0xDC | Communications: Bad Command Message Header |  |
| 221 | 0xDD | Communications: Bad Command Stem |  |
| 222 | 0xDE | Communications: Bad Upload Checksum |  |
| 223 | 0xDF | Communications: Bad Upload Address |  |
| 224 | 0xE0 | Communications: Command Queue Overflow |  |
| 225 | 0xE1 | SST Queue Overflow |  |
| 226 | 0xE2 | SST Queue Error: MET Already Active |  |
| 227 | 0xE3 | SST Queue Error: MET already passed |  |
| 228 | 0xE4 | Bad CIDP Data Block Number in Data Load Request |  |
| 229 | 0xE5 | Lost Sync. Pulse (Delphi) |  |

# (R_ECH) Command Echo. ApID=0x08

Every command sent to RPI has a corresponding RPI_ECHO package sent back as an acknowledgement. The structure of the Software Message package is given in Table 8.0-1.

Table 7.0-1 	RPI Command Echo format

|  | R_ECH Block |  |
| --- | --- | --- |
| Sec_2.1 | Sec_5.1 | Sec_8.1 | Sec_2.4 |
| Data Package Preamble | HK Header | Command Replica | Checksum |

## Command Replica

Table 7.1-1 	Command Replica

| Byte Count Offset | Byte Offset No | Byte Length | Description | Units | Range |
| --- | --- | --- | --- | --- | --- |
| 19 | 0 | 1 | Command stem | N/A | 0-255 |
| 20..23 | 1 | 4 | Command action Parameter 1 | N/A | Command specific |
| 24..27 | 5 | 4 | Command action Parameter 2 | N/A | Command specific |

# RPI Development Package Formats

The following sections introduce and describe the formats for development data packages produced by the RPI instrument in response to debugging commands.

# Development Package Formats

RPI responds to certain development commands by outputting Development Package(s) to the RS-422 port (to be received by CIDP, GSEOS, ASIST, etc.). All development packages are formatted as standard Science Data Packages, however, they are unlikely to be used during the mission time.

## ApID=0x1F Frequency Set Response Package

The frequency set command R_DEB_FREQ_SET is acknowledged by a message giving the programmed frequency, the coupler mode character, the relay settings for all four couplers, the synthesizer control byte settings, and the preselector control byte setting (see Table 9.1-1).

Table 8.1-1	Frequency Set Response package, ApID=0x1F

| Byte No. | Name | Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x1F |  |
| 5..6 | Byte Count | 21 | (constant) |
| 7-10 | Frequency | f<31:24> |  |
|  |  | f<23:16> | Sounding frequency in Hz. |
|  |  | f<15:8> |  |
|  |  | f<7:0> |  |
| 11 | Coupler mode | ‘N’ - normal ‘D’ - direct ‘C’ - calibrate ‘S’ - calibrate-direct | This character indicates whether a special coupler mode has been selected. |
| 12..13 | Xplus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 14..15 | Xminus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 16..17 | Yplus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 18..19 | Yminus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 20 | Reg5 |  |  | LO freq = Reg5*125 kHz |
| 21 | Reg4 |  | Synth. | + Reg4*125 khz / 28 |
| 22 | Reg3 |  | Control | + Reg3*125 kHz / 216 |
| 23 | Reg2 |  | Registers | + Reg2*125 kHz / 224 |
| 24 | Reg1 |  |  | + Reg1*125 kHz / 232 |
| 25 | Reg0 |  |  | + Reg0*125 kHz / 240 |
| 26 | Data Byte “n” | pfrq | Preselector control byte |
| 27 | Checksum |  | xor sum bytes 7-26 |

## ApID=0x2F Memory Read/Write Response Package

The memory read/write command reply gives the starting and ending addresses of the memory block followed by the contents of the block. The format for the memory read/write command reply message is given in Table 9.2-1.

Table 8.2-1	Memory Read/Write Response package, ApID=0x2F

| Byte No. | Name | Byte Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x2F |  |
| 5..6 | Byte Count |  | Byte Cnt = 10 + 4*(Addr2-Addr1+1) |
| 7 | Data Byte 0 | ‘R’ or ‘W’ | ‘R’ = memory block read, ‘W’ = memory block write |
| 8..11 | Starting Address | <31:24> <23:16> <15:8> <7:0> | Starting address of memory block to be read/written |
| 12..15 | Ending Address | <31:24> <23:16> <15:8> <7:0> | Ending address of memory block to be read/written |
| 16..19 | Data 1 | <31:24> <23:16> <15:8> <7:0> | 32 bit word |
| … | … | … | … |
| 15+4*n |  | Checksum | xor sum bytes 7-19 |

## ApID=0x3F VME Read/Write Response Package

The VME Read/Write response package returns the VME address and contents for the affected VME port.  The format for the VME read/write command reply message is given in Table 9.3-1.

Table 8.3-1	VME Read/Write Response package, ApID=0x3F

| Byte No. | Name | Byte Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x3F |  |
| 5..6 | Byte Count | 6 |  |
| 7..10 | Address | <31:24> <23:16> <15:8> <7:0> | VME Address of affected VME port.. |
| 11 | Value |  | Contents of affected VME port after VME Port command is executed. |
| 12 | Checksum |  | xor sum bytes 7-11 |

## ApID=0x4F Digitizer Samples Package

The R_DEB_DGTZ_GET command continuously takes digitizer samples, sending back digitizer sample blocks as indicated below. Packages are transmitted continuously until RPI receives a new command.  The format for the Digitizer Samples package is shown in Table 9.4-1.

Table 8.4-1	Digitizer Sample package, ApID=0x4F

| Byte No. | Name | Byte Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x4F |  |
| 5..6 | Byte Count | 4N+1 | N = number of complex samples |
| 7..8 | Real 1 | <15:8> <7:0> | First real sample |
| 9..10 | Imaginary 1 | <15:8> <7:0> | First imaginary sample |
| 11..12 | Real 2 | <15:8> <7:0> | Second real sample |
| 13..14 | Imaginary 2 | <15:8> <7:0> | Second imaginary sample |
| … | … | … | … |
|  | Real N | <15:8> <7:0> | Nth real sample |
|  | Imaginary N | <15:8> <7:0> | Nth imaginary sample |
| 4N+6 | Checksum |  | xor sum |

# Appendix A. Thermal Noise Data Processing

Since lots of effort has been put into making standard reusable tools for operational software and data analysis software we would like to find a way to structure the TTD output telemetry packages to use the DataBin format (i.e. General header, preface, data header, frequency header and data block).  In order to force TTD data into this DataBin file handling convention without paying too dearly in storage efficiency, we have defined a standard TTD mode of operation, making N=3 the minimum value allowed.  This ensures that we have at least 32 time domains samples per frequency step.  Note, that for standard sounder modes, all of these values correspond to samples after a single pulse. However, the TTD mode is a Receive Only mode, so there is no transmitted pulse, but there is still a logic pulse that triggers the digitizer to make a one-dimensional sample array of 32 to 1024 samples at each frequency step.  The elements of the DataBin are 8-bit Logarithmic amplitudes, 8-bit cross-power log ampliltudes, and the corresponding cross-power phase arguments also in an 8-bit format (0-359 deg in 1.4deg steps).  The algorithm for computing these out of 36 samples (S0 to S35) on each of three antennas (Sx0 to Sx35; Sy0 to Sy35; Sz0 to Sz35) is:

## Calculating Log Amplitudes

Compute a power term for each complex sample from Receiver X,

Px =  Re2 + Im2	(A-1)

Note that the power term is always positive, so we can add without concern that the amplitude of the sum may be cancelled out by anti-phased signals.  Therefore, sum the first 8 contiguous powers,

8Px = ( Pi , for i = 0 to 7	(A-2)

Now make the log of the average positive power term:

Ax  = 10 log (8Px) - 9.031	(A-3)

where the -9.031 divides the power by a factor of 8, thus forming the first average, Ax[0].  Now move the starting point up 4 samples, and create a new 8-point average which overlaps half the data used in the previous average.  Continue up until sample 28 to 35 are used in making the eighth average, the final amplitude stored in the data bin. Store Ax[0] to Ax[7] in the databin.

Repeat for Ay[0-7] and Az[0-7].

## Calculating Cross Power Terms (XY, XZ and YZ)

Using all 36 samples, compute a cross-power for each pair of complex samples,

Pxy = (Re(Sxi) + j Im(Sxi)) * (Re(Syi) - j Im(Syi))	(A-4)

which are sampled simultaneously from antenna X &Y, or X & Z or Y & Z, then coherently sum (actually average by dividing by 36) the 36 complex products.  Conjugating the Y samples gives the cross-power vector a phase equal to the phase difference between the X axis and Y axis sample.  Since the signals have the receiver calibration corrections as well as the spin-phase rotation correction already performed, the X Y and Z signal components are already lined up with the RPI coordinate system, and the combined amplitude of the cross-products is representative of the real E-field strengths.

Real(Sum) =  (Real(Si) / 36) for i = 0 to 35, and 	(A-5)

Imag(Sum) =  (Imag(Si) / 36) for i = 0 to 35

Note: These power terms need not be positive numbers, but since they are already powers (not amplitudes) we have to compute a resultant vector using  sqrt(Re2 + Im2) in order to express the magnitude of the cross-power in dB.

Mag|CXY| = (sqrt( (Real(Sum))2 + (Imag(Sum)) 2 )	(A-6)

And in dB,

CXY Power = 10 log (Mag|CXY|)	(A-7)

## Calculating Cross Phases (XY, XZ and YZ)

Phase CXY uses the cross-power vector components Re(Sum) and Im(Sum)

PhaseCXY = tan-1 (Im(Sum)/Re(Sum)),   [range -180deg to +179deg]	(A-8)

And the conversion to 8-bit phase is,

CXY Phase = (256/360) (PhaseCXY+180)	(A-9)

# Appendix B. Coupler Band Center Frequency Table

| Index | Frequency, kHz | Index | Frequency, kHz | Index | Frequency, kHz |
| --- | --- | --- | --- | --- | --- |
| 0 | 3.000 | 46 | 45.600 | 92 | 193.500 |
| 1 | 9.500 | 47 | 47.150 | 93 | 195.000 |
| 2 | 9.900 | 48 | 48.700 | 94 | 195.750 |
| 3 | 10.200 | 49 | 51.600 | 95 | 198.000 |
| 4 | 10.450 | 50 | 54.500 | 96 | 200.000 |
| 5 | 10.800 | 51 | 56.025 | 97 | 205.000 |
| 6 | 11.150 | 52 | 57.550 | 98 | 220.000 |
| 7 | 11.600 | 53 | 59.425 | 99 | 233.000 |
| 8 | 11.950 | 54 | 61.300 | 100 | 259.000 |
| 9 | 12.500 | 55 | 63.325 | 101 | 308.000 |
| 10 | 13.100 | 56 | 65.350 | 102 | 320.000 |
| 11 | 13.500 | 57 | 68.300 | 103 | 380.000 |
| 12 | 13.750 | 58 | 72.700 | 104 | 440.000 |
| 13 | 14.300 | 59 | 74.550 | 105 | 496.000 |
| 14 | 14.750 | 60 | 76.400 | 106 | 535.000 |
| 15 | 15.350 | 61 | 78.850 | 107 | 575.000 |
| 16 | 15.800 | 62 | 81.200 | 108 | 605.000 |
| 17 | 16.500 | 63 | 84.900 | 109 | 630.000 |
| 18 | 17.350 | 64 | 86.000 | 110 | 653.000 |
| 19 | 17.900 | 65 | 89.800 | 111 | 685.000 |
| 20 | 18.300 | 66 | 97.400 | 112 | 760.000 |
| 21 | 18.950 | 67 | 100.500 | 113 | 870.000 |
| 22 | 19.600 | 68 | 102.500 | 114 | 904.000 |
| 23 | 20.400 | 69 | 105.000 | 115 | 973.000 |
| 24 | 21.000 | 70 | 108.000 | 116 | 1190.000 |
| 25 | 21.950 | 71 | 111.500 | 117 | 1220.000 |
| 26 | 23.000 | 72 | 114.000 | 118 | 1280.000 |
| 27 | 23.700 | 73 | 118.200 | 119 | 1320.000 |
| 28 | 24.150 | 74 | 134.500 | 120 | 1510.000 |
| 29 | 25.050 | 75 | 137.500 | 121 | 1600.000 |
| 30 | 25.900 | 76 | 139.750 | 122 | 2000.000 |
| 31 | 26.900 | 77 | 143.500 | 123 | 3000.000 |
| 32 | 27.700 | 78 | 146.000 |  |  |
| 33 | 28.900 | 79 | 149.500 |  |  |
| 34 | 30.600 | 80 | 151.500 |  |  |
| 35 | 31.600 | 81 | 154.500 |  |  |
| 36 | 32.300 | 82 | 172.000 |  |  |
| 37 | 33.500 | 83 | 174.000 |  |  |
| 38 | 34.500 | 84 | 175.500 |  |  |
| 39 | 35.900 | 85 | 177.000 |  |  |
| 40 | 37.000 | 86 | 180.000 |  |  |
| 41 | 38.700 | 87 | 182.500 |  |  |
| 42 | 40.400 | 88 | 185.000 |  |  |
| 43 | 41.600 | 89 | 186.000 |  |  |
| 44 | 42.550 | 90 | 190.500 |  |  |
| 45 | 44.075 | 91 | 192.000 |  |  |

# Appendix C. Calibration Procedures

## Phase calibration procedure

Phase calibration was done at SwRI labs by feeding a known generator signal into three receivers set at G=15, as shown on Figure C1-1.

Figure C1-1 	Phase calibration setup with HP synthesizer

The output of each receiver was sampled twice, to capture I and Q quadrature components spaced 90( apart. The ratio of Z channel output to X and Y channels comprises the default calibration table.

## Onboard calibration procedure

Onboard calibration procedure is done by feeding identical calibration signals to the receivers on each frequency before the actual transmission is made, as shown in Figure C2-1. The calibration signal is applied directly to the couplers at the base of the X and Y antennas; however, the Z channel is calibrated without the wide-band pre-amplifiers whose gain is assumed equal to 12 dB (LoGain setting) and phase contributions are assumed constant for the mission period. The amplitude of the calibration signals is always the same and is selected optimally to obtain good receiver responses with any setting of their gain.

The receiver response to the calibration signals is used onboard to introduce corrections to the X and Y channel data that equalize their phase and gain characteristics with the Z channel. It is important to make +12 dB corrections to the X and Y data on the ground if HiGain setting was used for the Z preamplifier. With this correction introduced, RPI data can be directly used to derive the angles of arrival. An additional effort is required to convert the observed amplitudes to the physical units, [nV/m], as discussed in Section 3.2.1.

Figure C2-1 	Application of calibration signals to X(Y) and Z receiver channels

## Amplitude calibration procedure

Amplitude calibration was done at SwRI labs by feeding a known generator signal into receiver as shown on Figure C3-1.

Figure C3-1 	Amplitude calibration setup with HP synthesizer

### Input voltage calculation

The generator input was originally expressed in [dBm into a 50 ohm load]. The following considerations are used to express the input voltage in [Vp]:

- dBm units are referenced to 1 mW of power on 50 ohm load

- Voltage corresponding to 1 mW on 50 ohm  is:

- For D dBm the generator output voltage is

Vg-out,p = Vref, p *10(D/20) = *10(D/20) [V]

To account for the fact that the calibration setup (Figure C1-1) is different from the operational RPI setup where both dipole elements feed the receiver, 6 dB are subtracted from the test source power. Another 6 dB are subtracted to account for the losses in the 3 way splitter. Thus, the input voltage for this test is

To obtain the value of receiver sensitivity in volts per digitizer unit, Sdu,p(f), from the amplitude calibration data, the following formula is used:

[V/unit],

where Dout(f) are the amplitudes [in digitizer units] and Vin,p is the peak voltage in [V].

### Amplitude calibration coefficients

Ratio of Z channel amplitudes to X and Y channel amplitudes gives the correction coefficients and  for the re-calibration procedure described in Section 3.2.2.6. The coefficients are given in the Table C3-1.

### Physical Units table

Figure C3-1 shows graph of the Z channel zero-to-peak voltage per digitizer unit, in [nV/unit], which is used for conversion of the amplitudes to physical units in Section 3.2.2.8.

Figure C3-2 	Z channel voltage per digitizer unit, [nV].

The gains of the X and Y channels are matched to the gain of the Z receiver during onboard calibration (see Section 3.1.2) so that, for the purpose of conversion to physical units, X and Y digitizer unit values are not used. The zero-to-peak voltage [in nV] per digitizer units for Z channel are given in Table C3-1. Section 3.2.2.3 explains how to use these coefficients to derive the Physical Units table for all channels and all settings of the base gain.

Table C3-1	X/Y Amplitude Corrections and Physical Units table.

| Frequency[kHz] | Correction coefficient | Correction coefficient | Voltage per digitizer unit [nVp] |
| --- | --- | --- | --- |
| 7 | 36.786 | 34.606 | 1.971 |
| 8 | 32.217 | 27.144 | 1.691 |
| 9 | 21.343 | 17.426 | 1.712 |
| 10 | 20.693 | 36.123 | 1.549 |
| 11 | 26.149 | 44.490 | 1.168 |
| 12 | 20.990 | 24.373 | 1.777 |
| 13 | 9.402 | 13.094 | 4.328 |
| 14 | 15.622 | 18.961 | 3.123 |
| 15 | 13.994 | 12.361 | 3.653 |
| 16 | 11.783 | 8.955 | 2.784 |
| 17 | 33.190 | 17.836 | 1.448 |
| 18 | 22.553 | 42.523 | 1.343 |
| 19 | 17.918 | 15.358 | 1.933 |
| 20 | 16.976 | 31.871 | 1.961 |
| 21 | 6.800 | 21.410 | 3.704 |
| 22 | 17.677 | 16.946 | 2.885 |
| 23 | 17.989 | 19.127 | 1.632 |
| 24 | 13.724 | 37.506 | 1.466 |
| 25 | 19.310 | 49.934 | 1.404 |
| 26 | 13.823 | 30.128 | 2.058 |
| 27 | 23.085 | 52.569 | 1.368 |
| 28 | 14.056 | 60.605 | 1.991 |
| 29 | 18.772 | 57.071 | 1.976 |
| 30 | 45.052 | 81.761 | 1.694 |
| 31 | 17.635 | 103.667 | 1.546 |
| 32 | 31.611 | 50.388 | 1.781 |
| 33 | 34.732 | 62.367 | 1.564 |
| 34 | 20.254 | 36.133 | 2.218 |
| 35 | 19.757 | 21.180 | 2.212 |
| 36 | 18.400 | 19.822 | 2.398 |
| 37 | 26.678 | 19.183 | 2.896 |
| 38 | 7.088 | 19.022 | 4.213 |
| 39 | 6.840 | 10.953 | 8.295 |
| 40 | 15.872 | 16.209 | 4.524 |
| 41 | 9.065 | 18.823 | 4.449 |
| 42 | 27.071 | 17.596 | 3.110 |
| 43 | 18.585 | 11.252 | 3.721 |
| 44 | 24.816 | 12.849 | 2.699 |
| 45 | 28.564 | 18.269 | 1.937 |
| 46 | 14.459 | 18.870 | 2.619 |
| 47 | 20.235 | 11.917 | 3.418 |
| 48 | 9.354 | 9.119 | 5.137 |
| 49 | 23.868 | 32.905 | 3.942 |
| 50 | 21.188 | 19.133 | 3.923 |
| 51 | 12.420 | 36.054 | 2.520 |
| 52 | 29.292 | 19.059 | 1.887 |
| 53 | 8.975 | 8.446 | 3.774 |
| 54 | 22.224 | 28.051 | 1.856 |
| 55 | 17.610 | 11.222 | 2.577 |
| 56 | 11.562 | 6.374 | 5.239 |
| 57 | 29.261 | 22.636 | 2.672 |
| 58 | 21.563 | 22.680 | 3.942 |
| 59 | 25.213 | 59.568 | 1.785 |
| 60 | 45.268 | 35.479 | 1.742 |
| 61 | 15.244 | 45.731 | 2.230 |
| 62 | 24.538 | 48.890 | 1.739 |
| 63 | 13.188 | 30.593 | 3.304 |
| 64 | 35.684 | 33.205 | 2.042 |
| 65 | 9.342 | 11.769 | 4.424 |
| 66 | 11.581 | 16.730 | 3.539 |
| 67 | 17.590 | 36.974 | 2.428 |
| 68 | 15.297 | 22.594 | 2.854 |
| 69 | 11.875 | 17.102 | 3.738 |
| 70 | 25.838 | 25.037 | 3.704 |
| 71 | 10.403 | 12.801 | 5.942 |
| 72 | 22.157 | 12.810 | 4.977 |
| 73 | 30.716 | 27.777 | 3.865 |
| 74 | 14.420 | 18.720 | 4.281 |
| 75 | 8.577 | 17.863 | 4.946 |
| 76 | 13.445 | 30.042 | 2.465 |
| 77 | 22.596 | 41.567 | 2.249 |
| 78 | 49.523 | 29.462 | 2.037 |
| 79 | 14.400 | 11.364 | 4.022 |
| 80 | 16.653 | 10.077 | 4.375 |
| 81 | 34.891 | 39.038 | 2.356 |
| 82 | 18.386 | 9.488 | 4.740 |
| 83 | 25.315 | 39.431 | 2.342 |
| 84 | 15.746 | 23.405 | 3.250 |
| 85 | 18.788 | 15.823 | 5.812 |
| 86 | 40.319 | 18.063 | 4.169 |
| 87 | 43.113 | 19.452 | 3.884 |
| 88 | 39.570 | 34.594 | 3.884 |
| 89 | 19.636 | 33.790 | 3.224 |
| 90 | 25.350 | 14.358 | 4.236 |
| 91 | 3.019 | 29.121 | 3.670 |
| 92 | 25.115 | 33.200 | 2.315 |
| 93 | 21.976 | 37.368 | 2.645 |
| 94 | 8.724 | 10.383 | 12.639 |
| 95 | 63.335 | 93.084 | 2.435 |
| 96 | 29.208 | 34.685 | 6.221 |
| 97 | 19.591 | 26.168 | 12.251 |
| 98 | 32.935 | 33.748 | 8.209 |
| 99 | 34.474 | 15.712 | 12.639 |
| 100 | 27.344 | 24.015 | 8.125 |
| 101 | 13.214 | 9.863 | 16.251 |
| 102 | 23.919 | 16.358 | 7.884 |
| 103 | 12.607 | 12.284 | 11.710 |
| 104 | 17.867 | 19.526 | 8.209 |
| 105 | 16.077 | 10.988 | 9.368 |
| 106 | 16.228 | 13.966 | 7.110 |
| 107 | 12.299 | 14.229 | 7.731 |
| 108 | 15.828 | 14.383 | 6.474 |
| 109 | 25.354 | 17.031 | 5.729 |
| 110 | 17.699 | 17.278 | 7.731 |
| 111 | 16.565 | 14.466 | 10.341 |
| 112 | 12.685 | 10.554 | 8.209 |
| 113 | 14.753 | 10.991 | 10.209 |
| 114 | 10.074 | 14.180 | 10.080 |
| 115 | 11.926 | 7.943 | 10.908 |
| 116 | 21.001 | 12.682 | 6.806 |
| 117 | 20.359 | 10.752 | 8.382 |
| 118 | 6.305 | 9.523 | 16.251 |
| 119 | 16.798 | 26.434 | 6.581 |
| 120 | 23.307 | 16.712 | 5.204 |
| 121 | 19.995 | 12.782 | 6.270 |
| 122 | 23.611 | 15.531 | 6.422 |
| 123 | 18.062 | 16.589 | 9.594 |
| 124 | 17.703 | 21.532 | 5.855 |
| 125 | 9.714 | 8.704 | 7.884 |
| 126 | 14.386 | 22.749 | 5.942 |
| 127 | 25.434 | 18.045 | 4.915 |
| 128 | 17.767 | 15.616 | 9.153 |
| 129 | 28.002 | 24.155 | 5.104 |
| 130 | 8.663 | 9.238 | 10.080 |
| 131 | 6.312 | 6.178 | 13.970 |
| 132 | 6.728 | 9.394 | 15.024 |
| 133 | 6.933 | 7.804 | 14.746 |
| 134 | 7.136 | 6.298 | 13.496 |
| 135 | 17.465 | 19.682 | 9.049 |
| 136 | 13.504 | 11.332 | 6.924 |
| 137 | 15.085 | 9.126 | 8.750 |
| 138 | 6.499 | 11.481 | 14.478 |
| 139 | 11.321 | 9.636 | 8.562 |
| 140 | 12.798 | 20.977 | 8.043 |
| 141 | 13.108 | 18.182 | 7.963 |
| 142 | 6.574 | 9.818 | 14.746 |
| 143 | 12.421 | 18.075 | 8.562 |
| 144 | 9.433 | 8.350 | 9.954 |
| 145 | 25.469 | 11.797 | 7.373 |
| 146 | 13.652 | 10.816 | 7.305 |
| 147 | 21.252 | 16.727 | 8.655 |
| 148 | 32.431 | 13.486 | 5.492 |
| 149 | 6.883 | 6.569 | 11.540 |
| 150 | 16.721 | 12.934 | 5.273 |
| 151 | 6.155 | 6.172 | 10.477 |
| 152 | 17.773 | 13.965 | 7.174 |
| 153 | 10.568 | 9.557 | 6.806 |
| 154 | 13.076 | 10.216 | 9.153 |
| 155 | 19.648 | 21.449 | 5.812 |
| 156 | 14.772 | 9.907 | 7.731 |
| 157 | 26.792 | 12.853 | 5.898 |
| 158 | 12.733 | 21.769 | 6.173 |
| 159 | 13.038 | 8.004 | 8.295 |
| 160 | 15.014 | 23.208 | 6.320 |
| 161 | 21.317 | 20.401 | 6.748 |
| 162 | 13.308 | 21.225 | 6.691 |
| 163 | 12.567 | 10.689 | 12.065 |
| 164 | 7.428 | 5.338 | 11.710 |
| 165 | 15.918 | 13.064 | 5.008 |
| 166 | 8.476 | 8.772 | 9.954 |
| 167 | 14.371 | 12.777 | 5.647 |
| 168 | 8.184 | 7.510 | 8.209 |
| 169 | 10.648 | 10.248 | 6.865 |
| 170 | 27.222 | 19.983 | 5.104 |
| 171 | 6.976 | 8.006 | 10.617 |
| 172 | 6.718 | 12.690 | 10.341 |
| 173 | 14.378 | 12.360 | 5.309 |
| 174 | 10.088 | 9.784 | 8.655 |
| 175 | 14.863 | 18.483 | 7.884 |
| 176 | 12.483 | 18.235 | 8.043 |
| 177 | 10.726 | 14.817 | 7.807 |
| 178 | 6.011 | 6.876 | 13.054 |
| 179 | 20.914 | 9.667 | 6.748 |
| 180 | 12.001 | 16.022 | 7.110 |
| 181 | 12.981 | 18.420 | 6.806 |
| 182 | 3.598 | 12.192 | 6.527 |
| 183 | 20.221 | 24.183 | 6.270 |
| 184 | 8.837 | 8.129 | 8.848 |
| 185 | 7.423 | 5.022 | 14.746 |
| 186 | 13.141 | 7.956 | 9.594 |
| 187 | 12.939 | 7.524 | 13.496 |
| 188 | 9.553 | 10.438 | 13.271 |
| 189 | 6.351 | 11.512 | 8.295 |
| 190 | 8.857 | 13.676 | 12.065 |
| 191 | 11.366 | 6.615 | 10.908 |
| 192 | 6.168 | 10.970 | 13.729 |
| 193 | 7.907 | 12.212 | 10.209 |
| 194 | 11.308 | 7.620 | 12.639 |
| 195 | 15.911 | 11.273 | 6.748 |
| 196 | 10.366 | 12.281 | 7.110 |
| 197 | 7.774 | 14.434 | 9.480 |
| 198 | 6.820 | 11.903 | 11.710 |
| 199 | 6.612 | 8.034 | 12.639 |
| 200 | 39.178 | 53.870 | 1.602 |
| 201 | 13.195 | 12.727 | 11.375 |
| 202 | 6.252 | 7.386 | 12.251 |
| 203 | 5.333 | 7.015 | 13.729 |
| 204 | 11.540 | 14.550 | 8.382 |
| 205 | 6.451 | 11.460 | 13.054 |
| 206 | 19.874 | 12.594 | 6.527 |
| 207 | 10.833 | 9.087 | 11.540 |
| 208 | 11.365 | 8.220 | 16.251 |
| 209 | 11.273 | 8.372 | 11.215 |
| 210 | 22.545 | 10.323 | 7.963 |
| 211 | 14.340 | 11.332 | 6.924 |
| 212 | 6.980 | 7.098 | 11.885 |
| 213 | 14.365 | 13.972 | 6.748 |
| 214 | 18.743 | 14.399 | 5.688 |
| 215 | 6.263 | 6.066 | 12.251 |
| 216 | 11.234 | 6.054 | 13.729 |
| 217 | 17.927 | 11.291 | 6.370 |
| 218 | 16.620 | 12.561 | 6.924 |
| 219 | 16.209 | 12.157 | 9.049 |
| 220 | 10.645 | 10.417 | 7.110 |
| 221 | 22.216 | 13.233 | 7.373 |
| 222 | 9.361 | 9.140 | 8.295 |
| 223 | 11.781 | 11.733 | 7.807 |
| 224 | 7.809 | 8.239 | 11.540 |
| 225 | 13.115 | 7.217 | 9.480 |
| 226 | 6.507 | 10.706 | 11.710 |
| 227 | 4.035 | 14.873 | 8.382 |
| 228 | 14.663 | 16.396 | 8.295 |
| 229 | 10.957 | 9.745 | 7.174 |
| 230 | 13.139 | 18.744 | 5.492 |
| 231 | 11.834 | 11.529 | 5.898 |
| 232 | 12.752 | 13.951 | 5.309 |
| 233 | 8.394 | 8.014 | 8.750 |
| 234 | 12.885 | 27.991 | 5.417 |
| 235 | 6.729 | 8.967 | 10.341 |
| 236 | 10.190 | 10.953 | 8.295 |
| 237 | 26.762 | 16.533 | 6.032 |
| 238 | 14.062 | 14.998 | 6.422 |
| 239 | 13.386 | 9.494 | 8.382 |
| 240 | 11.912 | 20.756 | 6.474 |
| 241 | 13.413 | 18.000 | 8.043 |
| 242 | 9.755 | 9.809 | 12.639 |
| 243 | 6.640 | 11.110 | 19.422 |
| 244 | 17.871 | 11.150 | 8.750 |
| 245 | 19.177 | 17.905 | 6.924 |
| 246 | 21.714 | 11.418 | 8.471 |
| 247 | 4.921 | 5.308 | 18.959 |
| 248 | 8.019 | 8.019 | 11.375 |
| 249 | 10.867 | 12.097 | 8.750 |
| 250 | 9.960 | 12.411 | 9.368 |
| 251 | 7.454 | 6.610 | 13.970 |
| 252 | 12.782 | 11.337 | 7.584 |
| 253 | 13.741 | 25.793 | 7.373 |
| 254 | 10.781 | 12.100 | 10.080 |
| 255 | 6.464 | 6.250 | 13.970 |
| 256 | 13.647 | 22.912 | 7.963 |
| 257 | 12.972 | 8.741 | 13.729 |
| 258 | 13.304 | 13.905 | 10.617 |
| 260 | 6.005 | 3.632 | 24.898 |
| 270 | 9.431 | 6.415 | 15.068 |
| 280 | 14.246 | 7.391 | 11.156 |
| 290 | 10.847 | 8.204 | 10.752 |
| 300 | 12.588 | 7.026 | 12.986 |
| 310 | 21.019 | 13.570 | 10.316 |
| 320 | 12.645 | 5.383 | 15.790 |
| 330 | 14.396 | 12.438 | 13.527 |
| 340 | 8.071 | 5.989 | 16.220 |
| 350 | 11.127 | 6.334 | 15.081 |
| 360 | 14.185 | 7.170 | 10.393 |
| 370 | 14.406 | 8.015 | 12.407 |
| 380 | 12.546 | 7.335 | 10.632 |
| 390 | 5.538 | 3.951 | 26.371 |
| 400 | 4.226 | 5.123 | 24.318 |
| 410 | 11.859 | 7.906 | 10.096 |
| 420 | 9.283 | 6.814 | 14.680 |
| 430 | 5.134 | 3.738 | 34.714 |
| 440 | 11.886 | 10.814 | 16.694 |
| 450 | 5.419 | 3.888 | 23.333 |
| 460 | 9.923 | 6.501 | 14.926 |
| 470 | 11.018 | 6.068 | 21.529 |
| 480 | 12.622 | 4.512 | 20.657 |
| 490 | 4.186 | 4.568 | 28.879 |
| 500 | 12.762 | 9.662 | 17.978 |
| 510 | 6.934 | 5.365 | 17.008 |
| 520 | 8.096 | 6.064 | 20.086 |
| 530 | 15.782 | 9.848 | 14.645 |
| 540 | 8.360 | 6.349 | 15.278 |
| 550 | 9.609 | 13.985 | 14.496 |
| 560 | 15.908 | 15.854 | 10.749 |
| 570 | 16.476 | 14.520 | 9.011 |
| 580 | 12.335 | 10.969 | 17.339 |
| 590 | 16.389 | 10.443 | 14.639 |
| 600 | 8.679 | 3.668 | 25.418 |
| 610 | 10.504 | 11.823 | 15.054 |
| 620 | 7.686 | 5.708 | 15.401 |
| 630 | 11.699 | 9.945 | 13.936 |
| 640 | 9.394 | 7.385 | 12.102 |
| 650 | 8.641 | 7.266 | 13.649 |
| 660 | 5.147 | 6.420 | 24.133 |
| 670 | 10.500 | 7.525 | 19.637 |
| 680 | 5.899 | 5.443 | 16.740 |
| 690 | 11.646 | 7.234 | 17.254 |
| 700 | 7.315 | 4.102 | 24.787 |
| 710 | 20.112 | 5.407 | 23.588 |
| 720 | 7.770 | 2.583 | 68.821 |
| 730 | 4.549 | 6.102 | 49.537 |
| 740 | 3.487 | 4.105 | 74.168 |
| 750 | 5.608 | 3.872 | 30.909 |
| 760 | 3.231 | 4.666 | 24.081 |
| 770 | 7.055 | 4.718 | 23.472 |
| 780 | 9.058 | 5.052 | 36.278 |
| 790 | 8.240 | 7.505 | 21.753 |
| 800 | 9.705 | 4.202 | 29.687 |
| 810 | 10.111 | 10.224 | 18.353 |
| 820 | 10.725 | 11.547 | 15.085 |
| 830 | 13.357 | 12.610 | 15.337 |
| 840 | 7.370 | 6.775 | 26.837 |
| 850 | 8.788 | 4.528 | 22.722 |
| 860 | 6.852 | 8.163 | 22.084 |
| 870 | 10.045 | 8.069 | 14.374 |
| 880 | 7.056 | 7.056 | 23.909 |
| 890 | 9.935 | 7.108 | 15.566 |
| 900 | 8.285 | 4.498 | 24.177 |
| 910 | 7.471 | 5.942 | 24.695 |
| 920 | 10.427 | 7.085 | 15.555 |
| 930 | 83.906 | 14.703 | 14.461 |
| 940 | 14.034 | 8.285 | 21.931 |
| 950 | 20.491 | 9.025 | 18.007 |
| 960 | 17.326 | 10.957 | 22.342 |
| 970 | 13.099 | 10.088 | 14.597 |
| 980 | 9.927 | 7.120 | 22.223 |
| 990 | 15.436 | 5.756 | 23.764 |
| 1000 | 11.128 | 5.875 | 25.312 |
| 1010 | 8.934 | 5.790 | 31.958 |
| 1020 | 14.139 | 5.598 | 28.424 |
| 1030 | 7.726 | 3.159 | 40.426 |
| 1040 | 13.438 | 4.366 | 34.025 |
| 1050 | 12.553 | 3.194 | 34.428 |
| 1060 | 20.506 | 5.870 | 20.650 |
| 1070 | 5.595 | 3.223 | 34.696 |
| 1080 | 6.305 | 3.470 | 32.598 |
| 1090 | 7.968 | 6.390 | 32.455 |
| 1100 | 9.792 | 9.514 | 11.071 |
| 1110 | 10.004 | 5.325 | 15.847 |
| 1120 | 17.597 | 8.054 | 16.677 |
| 1130 | 16.327 | 8.679 | 12.671 |
| 1140 | 23.271 | 8.588 | 10.428 |
| 1150 | 10.912 | 5.540 | 14.980 |
| 1160 | 8.490 | 5.469 | 20.250 |
| 1170 | 10.175 | 4.211 | 19.562 |
| 1180 | 9.854 | 6.773 | 16.048 |
| 1190 | 15.427 | 10.767 | 10.995 |
| 1200 | 55.145 | 10.278 | 12.856 |
| 1210 | 11.495 | 4.431 | 21.696 |
| 1220 | 13.186 | 4.636 | 20.536 |
| 1230 | 23.027 | 12.315 | 11.417 |
| 1240 | 7.945 | 4.747 | 19.853 |
| 1250 | 19.740 | 10.518 | 14.867 |
| 1260 | 12.242 | 6.846 | 22.508 |
| 1270 | 16.123 | 10.157 | 15.716 |
| 1280 | 12.524 | 6.904 | 12.918 |
| 1290 | 14.368 | 5.578 | 17.021 |
| 1300 | 10.559 | 3.583 | 25.982 |
| 1310 | 8.321 | 11.487 | 13.421 |
| 1320 | 12.836 | 7.841 | 20.740 |
| 1330 | 15.849 | 10.231 | 13.727 |
| 1340 | 14.013 | 11.172 | 13.014 |
| 1350 | 18.286 | 9.131 | 12.547 |
| 1360 | 9.794 | 4.942 | 20.195 |
| 1370 | 11.634 | 5.776 | 23.892 |
| 1380 | 9.975 | 3.726 | 28.364 |
| 1390 | 13.429 | 8.453 | 17.730 |
| 1400 | 8.423 | 7.334 | 24.723 |
| 1410 | 11.832 | 6.333 | 19.392 |
| 1420 | 5.719 | 5.469 | 33.033 |
| 1430 | 15.598 | 8.610 | 17.820 |
| 1440 | 7.639 | 4.463 | 25.811 |
| 1450 | 10.007 | 5.672 | 20.948 |
| 1460 | 10.216 | 6.066 | 20.657 |
| 1470 | 7.441 | 5.346 | 29.859 |
| 1480 | 38.719 | 12.659 | 12.731 |
| 1490 | 15.110 | 13.443 | 11.441 |
| 1500 | 15.453 | 7.204 | 12.881 |
| 1510 | 9.255 | 5.450 | 17.259 |
| 1520 | 22.341 | 7.366 | 13.259 |
| 1530 | 17.859 | 10.047 | 11.145 |
| 1540 | 11.766 | 12.660 | 11.056 |
| 1550 | 15.502 | 10.655 | 11.832 |
| 1560 | 23.361 | 11.015 | 14.840 |
| 1570 | 12.000 | 8.829 | 19.120 |
| 1580 | 16.733 | 9.917 | 12.782 |
| 1590 | 24.856 | 8.650 | 14.758 |
| 1600 | 20.929 | 10.446 | 10.616 |
| 1610 | 24.382 | 10.715 | 13.913 |
| 1620 | 13.658 | 7.647 | 16.677 |
| 1630 | 27.832 | 7.793 | 15.013 |
| 1640 | 15.107 | 5.058 | 24.282 |
| 1650 | 15.240 | 7.583 | 16.173 |
| 1660 | 9.587 | 4.911 | 25.217 |
| 1670 | 16.256 | 5.645 | 22.179 |
| 1680 | 10.434 | 5.404 | 23.621 |
| 1690 | 20.190 | 11.801 | 15.783 |
| 1700 | 16.985 | 14.257 | 14.288 |
| 1710 | 18.762 | 6.351 | 22.877 |
| 1720 | 16.314 | 9.970 | 20.682 |
| 1730 | 14.882 | 10.098 | 17.165 |
| 1740 | 9.748 | 7.070 | 19.978 |
| 1750 | 18.362 | 7.462 | 19.978 |
| 1760 | 16.568 | 8.525 | 16.275 |
| 1770 | 25.735 | 11.713 | 15.716 |
| 1780 | 17.243 | 10.324 | 17.425 |
| 1790 | 25.735 | 9.560 | 14.950 |
| 1800 | 21.279 | 6.938 | 19.900 |
| 1810 | 18.866 | 8.871 | 15.555 |
| 1820 | 30.486 | 10.303 | 14.176 |
| 1830 | 10.831 | 5.824 | 23.680 |
| 1840 | 24.130 | 11.531 | 17.317 |
| 1850 | 32.220 | 12.879 | 14.294 |
| 1860 | 14.236 | 11.589 | 19.104 |
| 1870 | 20.762 | 8.586 | 16.339 |
| 1880 | 21.271 | 9.771 | 16.665 |
| 1890 | 20.983 | 13.964 | 15.581 |
| 1900 | 21.163 | 7.062 | 20.562 |
| 1910 | 33.354 | 13.330 | 15.764 |
| 1920 | 22.529 | 11.792 | 16.974 |
| 1930 | 24.196 | 6.926 | 22.676 |
| 1940 | 15.450 | 8.283 | 21.161 |
| 1950 | 21.298 | 9.241 | 20.863 |
| 1960 | 15.847 | 7.984 | 22.120 |
| 1970 | 16.708 | 9.300 | 23.456 |
| 1980 | 18.155 | 10.785 | 19.308 |
| 1990 | 27.439 | 10.340 | 15.537 |
| 2000 | 20.660 | 10.024 | 22.622 |
| 2010 | 20.151 | 10.621 | 21.446 |
| 2020 | 19.490 | 11.485 | 21.439 |
| 2030 | 24.855 | 12.918 | 17.507 |
| 2040 | 44.388 | 15.294 | 16.339 |
| 2050 | 44.719 | 11.430 | 15.010 |
| 2060 | 23.496 | 10.559 | 22.194 |
| 2070 | 31.536 | 10.387 | 22.231 |
| 2080 | 19.094 | 8.239 | 22.327 |
| 2090 | 27.660 | 13.077 | 16.411 |
| 2100 | 24.789 | 9.566 | 18.995 |
| 2110 | 20.502 | 10.019 | 21.982 |
| 2120 | 23.006 | 13.403 | 19.314 |
| 2130 | 26.375 | 11.497 | 17.590 |
| 2140 | 21.260 | 11.135 | 16.307 |
| 2150 | 25.100 | 10.565 | 16.871 |
| 2160 | 28.372 | 14.285 | 15.444 |
| 2170 | 28.702 | 12.349 | 14.853 |
| 2180 | 25.367 | 15.240 | 16.694 |
| 2190 | 28.563 | 18.720 | 14.251 |
| 2200 | 17.094 | 10.119 | 25.633 |
| 2210 | 29.791 | 16.614 | 14.607 |
| 2220 | 27.706 | 10.307 | 18.218 |
| 2230 | 28.496 | 13.667 | 15.376 |
| 2240 | 35.033 | 15.256 | 13.341 |
| 2250 | 19.134 | 9.728 | 21.838 |
| 2260 | 23.721 | 16.005 | 17.272 |
| 2270 | 24.485 | 11.318 | 17.530 |
| 2280 | 23.678 | 10.983 | 17.303 |
| 2290 | 22.605 | 11.817 | 18.364 |
| 2300 | 30.133 | 12.917 | 15.064 |
| 2310 | 27.029 | 11.162 | 17.420 |
| 2320 | 25.156 | 14.553 | 17.916 |
| 2330 | 22.827 | 14.063 | 19.465 |
| 2340 | 26.014 | 14.991 | 17.834 |
| 2350 | 23.838 | 19.029 | 14.543 |
| 2360 | 28.934 | 14.879 | 14.635 |
| 2370 | 26.372 | 16.091 | 16.615 |
| 2380 | 30.514 | 18.837 | 13.971 |
| 2390 | 24.486 | 16.397 | 17.294 |
| 2400 | 23.373 | 16.356 | 17.416 |
| 2410 | 28.109 | 14.547 | 15.588 |
| 2420 | 33.236 | 19.531 | 13.093 |
| 2430 | 28.522 | 16.096 | 17.697 |
| 2440 | 34.712 | 16.634 | 12.623 |
| 2450 | 30.599 | 18.734 | 15.274 |
| 2460 | 25.800 | 17.529 | 16.196 |
| 2470 | 29.656 | 18.546 | 13.815 |
| 2480 | 32.854 | 16.769 | 13.065 |
| 2490 | 27.569 | 17.346 | 15.156 |
| 2500 | 31.357 | 17.022 | 13.238 |
| 2510 | 27.330 | 17.652 | 15.922 |
| 2520 | 27.369 | 18.414 | 15.790 |
| 2530 | 28.882 | 19.299 | 14.963 |
| 2540 | 26.054 | 13.548 | 16.935 |
| 2550 | 27.661 | 17.956 | 16.064 |
| 2560 | 32.971 | 20.663 | 12.844 |
| 2570 | 26.677 | 14.958 | 16.656 |
| 2580 | 25.225 | 13.706 | 17.740 |
| 2590 | 27.060 | 18.437 | 15.862 |
| 2600 | 26.859 | 18.006 | 15.661 |
| 2610 | 33.792 | 18.068 | 14.039 |
| 2620 | 26.937 | 14.877 | 17.223 |
| 2630 | 28.366 | 14.507 | 15.888 |
| 2640 | 28.266 | 13.289 | 17.716 |
| 2650 | 23.302 | 17.373 | 19.765 |
| 2660 | 27.276 | 15.803 | 18.506 |
| 2670 | 30.123 | 16.711 | 18.374 |
| 2680 | 25.276 | 16.762 | 19.812 |
| 2690 | 23.274 | 14.628 | 19.364 |
| 2700 | 33.492 | 24.340 | 15.316 |
| 2710 | 31.739 | 24.597 | 15.292 |
| 2720 | 30.819 | 17.004 | 15.994 |
| 2730 | 23.347 | 15.845 | 20.473 |
| 2740 | 31.319 | 22.923 | 15.617 |
| 2750 | 31.017 | 13.442 | 20.342 |
| 2760 | 31.151 | 19.499 | 16.467 |
| 2770 | 24.898 | 17.809 | 19.494 |
| 2780 | 28.714 | 17.870 | 17.721 |
| 2790 | 33.242 | 22.629 | 15.687 |
| 2800 | 33.293 | 19.662 | 15.926 |

# Footnotes

For frequencies below 300 kHz, the difference in the signal voltages induced in the X/Y antennas are (20.log(500/20) = 28 dB higher than in the Z antenna.

( RPI received voltages are defined as peak-to-ground, not rms. Vp corresponds to the amplitude of the phasors (the arrows shown in Figure 3.1-3).

# Text boxes

Figure 3.1-1 RPI onboard data processing.